## Slide 1: Announcement
Tomorrow’s office hr: CANCELLED!
  Email me for appointment!! PLEASE!
Show work!!
Quiz-7 and 8?

## Slide 2: Instruction Execution is … Simple, Even A Computer Can Do It
© Lawrence Snyder 2004
Remember Back To The Lightbot
Kelvin Sung
University of Washington, Bothell
(* Use/Modification with permission based on Larry Snyder’s CSE120)

## Slide 3: Recall Lightbot …
Our first discussion of Lightbot noted that the instructions were formed of composite operations …
Today … we see that computer’s instructions are, too

## Slide 4: Computers ...
4
Deterministically execute instructions to process information
    “Deterministically” means that when a computer chooses the next instruction to perform it is required by its construction to execute a specific instruction based only on the program and input it is given
Computers have no free will and they are not cruel

## Slide 5: Fetch/Execute Cycle
5
Computer = instruction execution engine
    The fetch/execute cycle is the process that executes instructions
The computer internal parts implement this cycle
Instruction Fetch (IF)
Instruction Decode (ID)
Data Fetch (DF)
Instruction Execution (EX)
Result Return (RR)

## Slide 6: Anatomy of a Computer
6
The Hard Disk is the a-device
Mouse
Keyboard
Scanner
Hard Disk
Floppy Disk
Monitor
Printer
Speakers
Memory
Output
ALU
Control
Input

## Slide 7: Memory ...
7
Programs and their data
must be in the memory
while they are running
0
G
1
o
2
D
3
a
4
w
5
g
6
s
7
!
8
!
9
0
10
...
11
0
byte=8 bits
1
0
0
0
1
0
0
memory addresses
Memory locations
memory contents
Groups of four bytes are a word
Memory
Output
ALU
Control
Input

## Slide 8: Control
8
Fetch/Execute cycle is
hardwired in computer’s
control; it’s the “engine”
The instructions executed have the form
ADDB 20, 10, 16
6
10
11
12
13
14
15
12
16
17
18
19
18
20
...
21
Put in memory location 20 the contents of memory location 10 + contents of memory location 16
Memory
Output
ALU
Control
Input

## Slide 9: Indirect Data Reference
9
Instructions tell where the data is, not what the data is … contents change
One instruction has many effects
ADDB 20, 10, 16
8
10
11
12
13
14
15
7
16
17
18
19
15
20
...
21
60
10
11
12
13
14
15
-55
16
17
18
19
5
20
...
21

## Slide 10: ALU
10
Arithmetic/Logic Unit
does the actual computing
Most computers have only about a 100-150 instructions hard wired
Each type of data has its own separate instructions
ADDB : add bytes ADDBU : add bytes unsigned
ADDH : add half words ADDHU : add halves unsigned
ADD : add words ADDU : add words unsigned
ADDS : add short decimal numbers
ADDD : add long decimal numbers
Memory
Output
ALU
Control
Input

## Slide 11: Input/Output
11
Input units bring data
to memory from outside world; output units send data to outside world from memory
    Most peripheral devices are “dumb” meaning that the processor assists in their operation
    Disks are memory devices because they can output information and input it back again
Memory
Output
ALU
Control
Input

## Slide 12: The PC’s PC
12
The program counter (PC) tells where the next instruction comes from
    Instructions are a word long, so add 4 to the PC to find the next instruction
2198
2199
2200
2201
2201
2203
2204
2205
2206
2207
2208
...
ADD 800, 428, 884
AND 414,418,720
Program Counter: 2200
OR
688,724

## Slide 13: Instruction Execution: The Setup
Run Instruction: 2200: Add 800, 428, 884

## Slide 14: Instruction Fetch: Get Some Work

## Slide 15: Instruction Decode: What To Do?

## Slide 16: Data Fetch: What’s The Input

## Slide 17: Instruction Execution: Just Do It

## Slide 18: Result Return: Put It Away 4 Future

## Slide 19: Clocks Run The Engine
19
The rate a computer “spins around” the Fetch/Execute cycle is controlled by it’s clock
    Current clocks run 2-3 GHz
    In principle, the computer should do one instruction per cycle, but often it fails to
    Modern processors try to do more than one instruction per cycle, and often succeed
Clock rate is not a good indicator of speed

## Slide 20: Intel
20

## Slide 21: Summary
21
Fetch/execute cycle runs instructions
  5 steps to interpret machine instructions
  Programs must be in the memory
  Data is moved in and out of memory
Instructions, data are represented in binary