## Slide 1
Approaches to Ambient Noise Characterization at Tidal Energy Sites
Chris Bassett, Brian Polagye, Jim Thomson
Northwest National Marine Renewable Energy Center
University of Washington
141st Meeting of the American Fisheries Society
Seattle, WA
September 6, 2011

## Slide 2
Need for Ambient Noise Characterization
Tidal energy projects will generate anthropogenic noise
  Sound propagates over long distances in the marine environment
  Potential to affect fish and marine mammal behavioral
Environmental impact depends on the context of other ambient noise
  Post-installation characterization
  Pre-installation baseline

## Slide 3
Sources of Noise
(NRC, 2003 as adapted from Wenz, 1962)
Natural
  Rain
  Surface waves and surf
  Bedload transport
  Biological
Anthropogenic
  Maritime traffic
  Active sonar
  Construction
  Aircraft
  Seismic exploration
Contamination
  Flow-noise
  Self-noise

## Slide 4
Characterization Methodologies
Study Area
Autonomous hydrophones on seabed (fixed)
Autonomous hydrophones on surface (drifting)
Cabled hydrophones at mid-water (drifting)

## Slide 5
Anthropogenic (Vessel) Noise
Variable spatial and temporal patterns
  Unique acoustic signatures
  Different source levels
Primary contribution to ambient noise budget

## Slide 6
Flow Noise
Caused by turbulent pressure fluctuations across hydrophone
  At 0.3 m/s, apparent at 20 Hz
  Frequency and intensity increases with current speed
  Masks ambient noise (up to 500 Hz)

## Slide 7
Flow Noise Suppression
Flow shields can mitigate flow noise during strong currents
Shield does not attenuate propagating noise up to (at least) 10 kHz
Unshielded
Shielded

## Slide 8
Bedload Transport
Noise source above 2 kHz during strong currents
(Hz)
(Thorne, 1986)
General agreement with theory
Notes: Spectra implies mobilization of sediments/gravel/cobbles 8 cm and smaller

## Slide 9
Seabed Hydrophones (Fixed)
20 Hz – 30 kHz
Autonomous hydrophone
Statistically well-resolved
2% duty cycle (over 3 months)
Susceptible to flow-noise
Sea Spider Instrumentation Package

## Slide 10
Surface Hydrophones (Drifting)
Continuous measurement
Unaffected by flow-noise
Convolution of temporal and spatial variability
Near-surface measurement

## Slide 11
Cabled Hydrophones (Drifting)
Computer
DAQ
Heave isolation
Hydrophone
Flow Shield
Pressure Logger
Anti-strum faring
Continuous measurement at depth
Convolution of temporal and spatial variability
Difficult to maintain deployment depth
Potential for contamination by cable strum, self-noise, and flow noise

## Slide 12
Context for Measuring Turbine Noise
Notes: Receiver 1200 m from vessel or turbine

## Slide 13
Conclusions
Baseline ambient noise assessments require “long-term” deployments
  Difficult to capture temporal variability with drifting measurements
  Differentiate between pseudo-sound (flow noise) propagating sound (bedload transport)
Drifting measurements best approach for “short-term” post-installation characterization
Anthropogenic sources are likely to drive the noise budget in populated coastal areas
Notes: Tidal turbines will likely only be audible at small ranges that are dependent on site specific ambient noise conditions.
At sites with significant existing anthropogenic noise noise from turbines will often be masked even at close ranges (< 1 km)

## Slide 14
Thank You
This material is based upon work supported by the Department of Energy, Snohomish County PUD, the National Science Foundation.
Field Engineers Joe Talbert and Alex DeKlerk
Captain Andy Reay-Ellers