## Slide 1
Developing Capabilities for Tidal Hydrokinetic Blade Strike Monitoring
Brian Polagye, Sharon Kramer, Sandra Parker-Stetter, and Jim Thomson
Northwest National Marine Renewable Energy Center
University of Washington
141st Meeting of the American Fisheries Society
Seattle, WA
September 6, 2011

## Slide 2
Tidal Energy Project Development
Proposed Project
60 m water depth
3.5 m/s peak currents
Cable to shore
2 x 6 m turbines
250 kW peak power
OpenHydro Turbines
Snohomish PUD/OpenHydro

## Slide 3
Environmental Concerns
 | Device presence: Static effects | Device presence: Dynamic effects | Chemical effects | Acoustic effects | Electromagnetic effects | Energy removal | Cumulative effects
Physical environment: Near-field |  |  |  |  |  |  | 
Physical environment: Far-field |  |  |  |  |  |  | 
Habitat |  |  |  |  |  |  | 
Invertebrates |  |  |  |  |  |  | 
Fish: Migratory |  |  |  |  |  |  | 
Fish: Resident |  |  |  |  |  |  | 
Marine mammals |  |  |  |  |  |  | 
Seabirds |  |  |  |  |  |  | 
Ecosystem interactions |  |  |  |  |  |  | 
Polagye, B., B. Van Cleve, A. Copping, and K. Kirkendall (eds), (2011) Environmental effects of tidal energy development.
Pilot-Scale Effects

## Slide 4
Dynamic Effects Monitoring
Quantify the risk of blade strike to marine life
Improve understanding of how marine life responds to device presence
Both of these should be at the lowest level of taxonomic classification possible
Laboratory and field studies to date suggest blade strike will be an infrequent occurrence
Monitoring should not alter behavior
Other projects have had limited success in improving our understanding of blade strike
Objectives
Challenges

## Slide 5
Possible Monitoring Approaches
 | Underwater Imaging | Active Acoustics | Trawl Surveys | Fish Tags
Prior MHK Experience | OpenHydro (EMEC) | Verdant Power (East River) ORPC (Cobscook Bay) | None | OpenHydro (FORCE)
Blade Strike Detection |  |  |  | 
Taxonomic Classification |  |  |  | 
Functional Range |  |  |  | 
Behavioral Disturbance |  |  |  | 
Overall |  |  |  | 
Illumination?
Turbidity?
Contrast?

## Slide 6
Underwater Imaging Considerations
Stereo imaging – absolute size, position, and speed
Similarities to trawl ground-truthing and benthic habitat surveys
  High relative motion between camera and target
  Taxonomic classification required
Several unique considerations for turbine monitoring
  Positioning of lights and cameras relative to turbine
  Long deployment time (biofouling, durability)
  Recovery and redeployment instrumentation

## Slide 7
Camera and Optics Selection
2 Mpx machine vision cameras
  ProSilica Manta G-201
  10 Hz maximum frame rate
  Resolution/bandwidth
45o FOV lens (in air)
Flat optical port (biofouling)
500 pixels/target
Chinook salmon
Source: Kresimir Williams, NOAA Fisheries
250 pixels/target
Chinook salmon?
125 pixels/target
Salmon
62 pixels/target
Fish?

## Slide 8
Illumination Selection
Imaging fast moving targets
  Short exposure time: 2-50 µs (Gallager, et al. 2004)
  Large camera-light separation (Jaffe 1988)
Full-spectrum strobes (Excelitas MVS 5002)
  Four strobes per stereo imaging system
Behavioral disturbance is problematic
  Considered red, IR, and NIR lighting options
  Initially, pre-set duty cycle with monitoring
  As behavior/interactions are better understood, progress to event-based illumination

## Slide 9
System Layout
2 stereo camera systems
  Strike detection
  Taxonomic classification
1 m camera-light separation
Compact frame for maintenance
Compact frame concept
Strobe housing
Stereo cameras
Main bottle
Power/Comms
Notes: Spectra implies mobilization of sediments/gravel/cobbles 8 cm and smaller

## Slide 10
Biofouling Mitigation
Biofilms formation begins immediately after deployment
Mechanical Wiper
Copper Ring
Ultraviolet Lighting
(capability)

## Slide 11
Recovery and Redeployment
Reasons for recovery:
Biofouling removal
Maintenance and repair
Additional instruments
Reorientation of cameras
Must be recovered independent of turbine
Must be reconnected to turbine power and data systems
Recovery frame
Mounting & alignment infrastructure
Compact frame concept

## Slide 12
Monitoring System Integration
Turbine Monitoring
Main Power and Communications
Junction Bottle
Stereo Imagers
Doppler profilers
CTDO
?
Power (400 V DC)
Fiber
Hydrophone Array
?
To Shore

## Slide 13
Discussion
How much emphasis should be placed on monitoring for blade strike?
  Laboratory tests suggest low likelihood
  How much species-to-species, site-to-site, and turbine-to-turbine variability is there?
Regulatory mandates are species-specific, but this limits the toolkit available to answer questions
Leverage environmental monitoring infrastructure whenever possible – camera can also monitor for fouling, damage, and vibration
Post-installation monitoring is essential, but technically challenging – need for prioritization

## Slide 14
Questions?
This material is based upon work supported by the Department of Energy and Snohomish County PUD.