## Slide 1
Integrated Post-Installation Monitoring
Brian Polagye
Northwest National Marine Renewable Energy Center
University of Washington
bpolagye@uw.edu
Monitoring Technologies and Strategies for Marine and Hydrokinetic Devices Webinar
September 14, 2011

## Slide 2
Tidal Energy Project Development
Proposed Turbines
60 m water depth
3.5 m/s peak currents
Low turbidity (< 1 NTU)
Cable to shore
2 x 6 m turbines
250 kW peak power
Gravity foundation
3-5 year deployment
OpenHydro Technology
Snohomish PUD/OpenHydro

## Slide 3
Post-Installation Monitoring
At pilot-scale, provide information about high significance/high uncertainty interactions with devices
  Key input to risk assessment frameworks
Monitoring should not change animal behavior nor affect device operation
Environmental monitoring should not dominate over other project costs
  All projects are also demonstrating technical readiness and economic viability
  Post-installation monitoring requires prioritization

## Slide 4
Polagye, B., B. Van Cleve, A. Copping, and K. Kirkendall (eds), (2011) Environmental effects of tidal energy development.
Commercial-Scale Effects
 | Device presence: Static effects | Device presence: Dynamic effects | Chemical effects | Acoustic effects | Electromagnetic effects | Energy removal | Cumulative effects
Physical environment: Near-field |  |  |  |  |  |  | 
Physical environment: Far-field |  |  |  |  |  |  | 
Habitat |  |  |  |  |  |  | 
Invertebrates |  |  |  |  |  |  | 
Fish: Migratory |  |  |  |  |  |  | 
Fish: Resident |  |  |  |  |  |  | 
Marine mammals |  |  |  |  |  |  | 
Seabirds |  |  |  |  |  |  | 
Ecosystem interactions |  |  |  |  |  |  | 
Environmental Concerns
Proposed monitoring for Snohomish PUD/OpenHydro demonstration

## Slide 5
Dynamic Effects Monitoring
Quantify the risk of blade strike to marine life
Improve understanding of how marine life responds to device presence
Both of these should be at the lowest level of taxonomic classification possible
Laboratory and field studies to date suggest blade strike will be an infrequent occurrence
Difficult and resource-intensive to monitor in the field
Objectives
Challenges

## Slide 6
Monitoring Technology
 | Underwater Imaging | Active Acoustics | Trawl Surveys | Fish Tags
Prior MHK Experience | OpenHydro (EMEC) | Verdant Power (East River) ORPC (Cobscook Bay) | None | OpenHydro (FORCE) Hydro Green (Hastings)
Blade Strike Detection |  |  |  | 
Taxonomic Classification |  |  |  | 
Functional Range |  |  |  | 
Behavioral Disturbance |  |  |  | 
Overall |  |  |  | 
Illumination
Turbidity and Aeration
Contrast
Tag Frequency

## Slide 7
Underwater Imaging Considerations
Stereo imaging – absolute size, position, and speed
Similarities to trawl ground-truthing and benthic habitat surveys
  High relative motion between camera and target
  Taxonomic classification required
Several unique considerations for turbine monitoring
  Positioning of lights and cameras relative to turbine
  Long deployment time (biofouling, durability)
  Recovery and redeployment instrumentation

## Slide 8
Camera and Optics Selection
2 Mpx machine vision cameras
  10 Hz maximum frame rate
  Resolution/bandwidth
45o FOV lens (in air)
Flat optical port (biofouling)
500 pixels/target
Chinook salmon
Source: Kresimir Williams, AK Fisheries Science Center
250 pixels/target
Chinook salmon?
125 pixels/target
Salmon
62 pixels/target
Fish?
Manta G-201 (to scale)

## Slide 9
Illumination Selection
Imaging fast moving targets
  Short exposure time: 2-50 µs (Gallager, et al. 2004)
  Large camera-light separation (Jaffe 1988)
Full-spectrum strobes (Excelitas MVS 5002)
  Four strobes per stereo imaging system
Behavioral disturbance is problematic
  Considered red, IR, and NIR lighting options
  Initially, pre-set duty cycle with disturbance analysis
  As behavior/interactions are better understood, progress to event-based illumination

## Slide 10
Biofouling Mitigation Strategies
Biofilm formation begins immediately after deployment
Mechanical Wiper
Copper Ring
Ultraviolet Lighting
Even with mitigation, performance will degrade with time

## Slide 11
System Layout Concept
2 stereo camera systems
  Strike detection
  Taxonomic classification
1 m camera-light separation
Compact frame for maintenance
Compact frame concept
Strobe housing
Stereo cameras
Main bottle
Power/Comms

## Slide 12
Recovery and Redeployment Concept
Reasons for recovery:
Biofouling removal
Maintenance and repair
Additional instruments
Reorientation of cameras
Must be recovered independent of turbine
Must be reconnected to turbine power and data systems
Recovery frame
Mounting & alignment infrastructure
Compact frame concept

## Slide 13
Monitoring System Integration
Turbine Monitoring
Main Power and Communications
Junction Bottle
Stereo Imagers
Doppler profilers
CTDO
?
Power and fiber disconnect
Hydrophone Array
?
To Shore
Marine life
Device condition
Wake
Inflow conditions
Water quality
Marine mammals
Device noise

## Slide 14
Discussion
How much emphasis should be placed on monitoring for blade strike?
  Laboratory tests suggest low consequence
  How much species-to-species, site-to-site, and turbine-to-turbine variability is there?
Regulatory mandates are species-specific, but this limits the tools available
Leverage environmental monitoring infrastructure whenever possible – camera can also monitor turbine health (biofouling, vibration)
Post-installation monitoring is essential, but technically challenging – prioritization required

## Slide 15
Acknowledgments
This material is based upon work supported by the Department of Energy and Snohomish County PUD.
This project leverages the expertise of many individuals:
University of Washington: Jim Thomson, Sandra Parker-Stetter, Joe Talbert, Alex de Klerk, Keith van Thiel, Tim McGinnis, Randy Sindelar, and Nick Stelzenmuller
H.T. Harvey & Associates: Sharon Kramer and David Zajanc
Sound & Sea Technology: Larry Armbruster
Sea Mammal Research Unit, Ltd: Dom Tollit, Jason Wood
Alaska Fisheries Science Center: Rick Towler and Kresimir Williams