## Slide 1
Developing Monitoring Capabilities for Tidal Hydrokinetic Energy Installations
Brian Polagye
Northwest National Marine Renewable Energy Center
University of Washington
NSF Workshop: Research at the Interface of Marine/Hydrokinetic Energy and the Environment
October 6, 2011

## Slide 2
Overview
Cabled monitoring: Dynamic effects
Discussion

## Slide 3
Pilot-Scale Monitoring
Gather information about device performance
Gather information about environmental interactions with potentially high significance at commercial scale
  Reduce uncertainty for risk assessment frameworks
  Basis for modifications to device design
Address regulatory and stakeholder concerns
Environmental monitoring principles
  Monitoring should not affect environmental receptors
  Monitoring should not affect device performance
  Costs must be in line with other aspects of projects

## Slide 4
Polagye, B., B. Van Cleve, A. Copping, and K. Kirkendall (eds), (2011) Environmental effects of tidal energy development.
Commercial-Scale Interactions
 | Device presence: Static effects | Device presence: Dynamic effects | Chemical effects | Acoustic effects | Electromagnetic effects | Energy removal | Cumulative effects
Physical environment: Near-field |  |  |  |  |  |  | 
Physical environment: Far-field |  |  |  |  |  |  | 
Habitat |  |  |  |  |  |  | 
Invertebrates |  |  |  |  |  |  | 
Fish: Migratory |  |  |  |  |  |  | 
Fish: Resident |  |  |  |  |  |  | 
Marine mammals |  |  |  |  |  |  | 
Seabirds |  |  |  |  |  |  | 
Ecosystem interactions |  |  |  |  |  |  | 
Pilot-Scale Monitoring Priorities
Need to understand stressor-receptor interactions first
Immeasurably small at pilot-scale
Small signal-to-noise ratio at pilot scale

## Slide 5
Site Overview
Proposed Turbines
3.5 m/s peak currents
Well-mixed water column
Low turbidity (< 1 NTU)
Scoured seabed: cobbles over consolidated sediment
Several runs of migratory fish (anadromous, e.g. salmon)
Marine mammals (cetaceans, pinnipeds)
Northern Admiralty Inlet, Puget Sound

## Slide 6
Project Overview
2 x 6 m turbines
250 kW peak power generation
Gravity foundation
55 m deployment depth
Cable to shore
3-5 year deployment, with maintenance every 1-2 years
OpenHydro Tidal Turbine
Site Developer: Snohomish PUD
Technology Provider: OpenHydro
Source: OpenHydro

## Slide 7
Overview
Cabled monitoring: Dynamic effects
Discussion

## Slide 8
Dynamic Effects Monitoring
Quantify the risk of blade strike to marine life
Improve understanding of how marine life responds to device presence
Both of these should be at the lowest level of taxonomic classification possible
Laboratory and field studies to date suggest blade strike will be an infrequent occurrence
Difficult and resource-intensive to monitor in the field
Objectives
Challenges

## Slide 9
Monitoring Technology Options
 | Underwater Imaging | Active Acoustics | Trawl Surveys | Fish Tags
Prior MHK Experience | OpenHydro (EMEC) | Verdant Power (East River) ORPC (Cobscook Bay) | OpenHydro (Puget Sound) ORPC (Cobscook Bay) | OpenHydro (FORCE) Hydro Green (Hastings)
Blade Strike Detection |  |  |  | 
Taxonomic Classification |  |  |  | 
Functional Range |  |  |  | 
Behavioral Disturbance |  |  |  | 
Overall |  |  |  | 
Illumination
Turbidity and Aeration
Contrast
Tag Frequency

## Slide 10
Stereo Imaging
500 pixels/target
Chinook salmon
Source: Kresimir Williams, AK Fisheries Science Center
250 pixels/target
Chinook salmon?
125 pixels/target
Salmon
62 pixels/target
Fish?
Provides absolute size, position, and speed
MHK-specific issues
  Long deployments (biofouling, corrosion)
  Maintenance
  Automated detection
Behavioral response to illumination is problematic
  Strobes required to minimize image blur
  Startle response or avoidance possible

## Slide 11
High Bandwidth Required
Chart: Bandwidth (MB/s)
| 5 Mpx | 2 Mpx | Imaging Sonar | Hydrophone array
Series 1 | 241.983 | 96 | 13 | 12
5 Mpx Stereo
2 Mpx Stereo
Imaging Sonar
Hydrophone Array
Target Res (Juvenile salmon at 3 m)
150 pixels/target
Gigabit Ethernet Capacity
100 pixels/target
Tetrahedral array sampling at 1 MHz

## Slide 12
Component Selection
Short exposure time: 2-50 µs (Gallager, et al. 2004)
Full-spectrum illumination
Investigating triggering approaches
Camera
Strobe
Allied Vision Manta G201
Excelitas MVS 5002
2 Mpx resolution
45 degree FOV lens (in air)
Flat optical port

## Slide 13
System Layout
2 stereo camera systems
  Rotor interaction
  Taxonomic classification
1 m camera-light separation
Compact frame for maintenance
Compact frame concept
Strobe housing
Stereo cameras
Main bottle
Power/Comms

## Slide 14
Biofouling Mitigation Strategies
Mechanical Wiper
Removal
Copper Ring
Biocide
Ultraviolet Light
Biocide
Even with mitigation, performance will degrade with time
Transparent Coating
Reduced Adhesion

## Slide 15
Recovery and Redeployment Concept
Reasons for recovery:
Biofouling removal
Maintenance and repair
Additional instruments
Reorientation of cameras
Must be recovered independent of turbine
Must be reconnected to turbine power and data systems
Recovery frame
Mounting & alignment infrastructure
Compact frame concept

## Slide 16
Monitoring System Integration
Turbine Monitoring
Power and Comms Distribution
Junction Bottle
Stereo Imagers
Doppler profilers
CTDO
?
ROV-mate power and fiber
Hydrophone Array
?
Export Cable
Marine life
Device condition
Wake
Inflow conditions
Water quality
Marine mammals
Device noise
Generated power
Power for monitoring
> 4 fiber optic channels

## Slide 17
Overview
Cabled monitoring: Dynamic effects
Discussion

## Slide 18
Discussion Points
Study prioritization is necessary given finite resources
  Appropriateness of studies may be site-specific
  How much emphasis should be placed on monitoring for blade strike?
Regulatory mandates are species-specific, but this limits available monitoring tools
Post-installation monitoring is technically challenging
  When possible, leverage dual-use infrastructure (e.g., cameras can also monitor turbine health)
  How much flexibility/modularity is required?
What is the best way to assess potentially significant interactions that cannot be monitored at pilot scale?

## Slide 19
Acknowledgments
This material is based upon work supported by the Department of Energy and Snohomish County PUD.
This project leverages the expertise of many individuals:
University of Washington: Jim Thomson, Sandra Parker-Stetter, Joe Talbert, Alex de Klerk, Keith van Thiel, Tim McGinnis, Randy Sindelar, and Nick Stelzenmuller
H.T. Harvey & Associates: Sharon Kramer and David Zajanc
Sound & Sea Technology: Larry Armbruster
Sea Mammal Research Unit, Ltd: Dom Tollit, Jason Wood
Alaska Fisheries Science Center: Rick Towler and Kresimir Williams

## Slide 20
Overview
Cabled monitoring: Dynamic effects
Autonomous monitoring: Acoustic effects
Discussion

## Slide 21
Effect of Turbine Noise on Marine Mammals
Harbor porpoises are known to avoid areas with high received levels of noise
  Exposures exceeding 140 dB re 1 µ Pa result in sustained avoidance (Southall et al. 2007)
During operation, turbine noise will increase broadband received levels to more than 140 dB re 1 µPa
Therefore, harbor porpoises (currently abundant) will display sustained avoidance of tidal turbines?
Use passenger ferry as a pre-installation source of opportunity for proxy study
  Broadband source level: 170±2 dB re 1 µPa at 1 m
  Similar frequency content to turbine noise

## Slide 22
Proxy Study of Harbor Porpoise
Study Site
Turbine Site
Closest Points of Approach by Passenger Ferry
AIS

## Slide 23
Response to Ferry – Presence/Absence
No apparent avoidance to 140 dB (broadband) received levels
Indicator of noise habituation
N = 16
R2 = 0.1, F = 5.5, p = 0.02