## Slide 1
Development of an Adaptable Monitoring Package for Marine Renewable Energy Projects
Part 1: Conceptual Design and Operation
Ben Rush, James Joslin, Andy Stewart, and Brian Polagye
University of Washington
Northwest National Marine Renewable Energy Center
MECs and the Environment: Monitoring
April 17, 2014

## Slide 2
Motivation: Environmental Risk Uncertainty
Discountable Risk
Significant Risk
Mitigate
Uncertain Risks
Monitor
“Retired” Risks
Identified Risks
Reduced Uncertainty
Monitoring Outcomes
Notes: On one end of the spectrum, discountable environmental risk – risks that we do not need further information to evaluate: Example: the volume of water displaced by a WEC raising coastal sea levels
On the other end of the spectrum, known significant environmental risk – risks that we know we need to mitigate against: Example: fuel release due to vessel collision with a MEC during maintenance – procedures and practices to prevent occurrence
In between – uncertain risks – might be discountable, might be significant. These are the risks that monitoring plans should be chipping away at.

## Slide 3
Risk Uncertainty Categories
Risk
Frequency of Occurrence
Severity of Outcome
X
=
Common Occurrence
Category X
? Severity ?
? Occurrence ?
Category Y
Severe Outcome
Notes: Category X: population consequences of acoustic disturbances (not MHK specific – general research problem)
Category Y: collision with an MEC – obviously MHK specific

## Slide 4
Reducing Category Y Risks
Category Y risks (unknown occurrence, severe outcome) are likely to be infrequent
Spatial comprehensive and temporally continuous monitoring of converters requires the least time to resolve risk
Data bandwidth for “brute force” approaches to this is problematic – “data mortgages”
Stereo-optical Cameras (2 Mpx @ 10 fps)
X
80 MB/s
X
3 months observations
=
600 TB of storage
Example: Continuous stereo-optical monitoring for a single camera pair. Comprehensive monitoring would require multiple pairs.

## Slide 5
Avoiding Data Mortgages
Neither pure hardware nor pure software solutions are likely to prevent data mortgages
Passive Acoustic Detection
Processing in near real-time
Omni-directional coverage at ranges on the order of 1 km
MEC
Split-beam Echosounder
Processing in near real-time
Tracking capability at ranges beyond 100 m
Optical Camera
Requires archival processing
Short range and limited field of view
Example: Detection, tracking, and identification of a marine mammal approaching a MEC

## Slide 6
Instrumentation Package Constraints
Data and Power Bandwidth
Cabled Package
MEC Export Cable
Close Coupling to MEC
Maintenance and Adaptability
Recoverable Package
and
Plug & Socket Approach

## Slide 7
Adaptable Monitoring Package (AMP)
“Socket”
“Plug”

## Slide 8
Instrument and Infrastructure Payload
Notes: Talk through each instrument and constraints

## Slide 9
Body Mechanical Design
Strobe Strut
Welded aluminum
Anodized as single piece
Fairing (not shown)
Hull and Frame
Engineered plastics (no corrosion risk and near-neutrally buoyant)
Longitudinal stiffening
Modular, swappable bulkheads

## Slide 10
Securement System
Mechanical securement (over-center toggles) – no power to stay engaged
For deployment, secure mechanically, then insert wet-mate connector
Resists currents > 5 m/s broadside to AMP

## Slide 11
AMP Integration: Tidal Energy
OpenHydro Open Centre turbine
(6 m diameter)
AMP
Notes: Now, how do we maintain it?

## Slide 12
Recovery/Deployment Options
Divers
ROV Servicing
Subsea Winch
Converter Recovery
Short work windows
Human safety risk
Short work windows
Minor modifications only
Moving parts in the ocean
Winch failure can cause catastrophic system failure
Can be expensive and risky

## Slide 13
AMP Operations Concept: Tidal Energy
AMP and Deployment ROV
Launch Platform
Umbilical
Current Direction
Notes: Why umbilical and launch platform? Don’t have the ROV fight drag its umbilical in the upper water column – reserve thrust to deploy package
Why against currents? Passive safety

## Slide 14
“Millennium” Falcon Deployment System
Inspection-class ROV
4 Vectored Thrusters
“Millennium” Skid
6 Thrusters
  4 Vectored
  2 Vertical
Docking alignment
Securement actuators
Power and comms (SeaView)
SAAB Seaeye Falcon
Notes: Objective: provide work-class thrust capabilities with simplicity of deployment for an inspection-class ROV
“Stock” ROV + custom skid – stock system has insufficient thrust and provides none of the functions needed to facilitate docking and securement
Discuss vectored thrusters – sideways parking job + rotation
SeaView “Raptor” skid

## Slide 15
System Stability
Center of Pressure
Center of Thrust
Axis of Rotation
Center of Thrust and Center of Pressure
  Vertical alignment to prevent pitching
  Horizontal separation may be undesirable
Center of Mass and Center of Buoyancy
  Vertical separation for stability
  Horizontal alignment by trimming
Axis of rotation
Notes: Identifying center of pressure requires detailed hydrodynamic analysis – James up next

## Slide 16
System Testing
Testing progression
  Tank tests (late spring)
  Lake field tests (mid-summer)
  Open-ocean field tests (fall)
Rehearse operations and make engineering corrections
  Package trim
  Stabilizer fins
  ROV umbilical management

## Slide 17
Discussion
Integration with WEC monitoring missions
  AMP and Millennium Falcon are critical infrastructure for PMEC-SETS
Non-monitoring applications
  “Plug and socket” architecture for maintenance of critical undersea components
Docking enhancement
  ROV piloting force feedback

## Slide 18
Summary
Integrated instrumentation packages will play a critical role in reducing environmental risk without incurring large data mortgages
Package design requires a significant systems engineering effort
Notes: Plug Andrea’s session on “Big Data”

## Slide 19
Acknowledgements
This material is based upon work supported by the Department of Energy under FG36-08GO18179-M001 and Snohomish Public Utility District.
The AMP represents the engineering efforts of the authors, as well as a broader team including Paul Gibbs (APL), Chris Siani (APL), Trina Lichtendorf (APL), Tom Jackson (Jackson Engineering), and Danny Miles (Snohomish PUD).
Thanks also to Andrea Copping (PNNL) for many productive discussions about environmental risks.