## Slide 1: Why do Cross-Flow Turbines Stall?
Robert J. Cavagnaro*, Benjamin Strom, Alberto Aliseda, Brian Polagye
University of Washington
NNMREC
rcav@uw.edu
Notes: Stall defined as inability to rotate

## Slide 2: Motivation
Critical λ
Stable
Stalls under torque control
Does stall occur immediately at critical TSR?
Does turbulence play a role?
Notes: Split in two – torque(theta) speed(theta): Show Cq(tsr) with shaded regions or arrows under torque control
Motivations: Peaks of the Cq curve is the limit of stable operation for this type of turbine – point at which a fluctuation of a sizeable enough intensity will cause ‘catastrophic stall’, not to be confused with dynamic stall. Under torque control, turbine will stall here, but it’s close to the peak power performance point. We’d like to understand why the turbine stalls at this point for several reasons: 1. to build more robust torque controllers capable of stable operation near peak Cq point (there is some uncertainty in peak Cp point, can change over time) 2. to be able to more accurately simulate or emulate the dynamics of such a turbine operating near stall. 3. for Region 3 control – shedding power moving to the left of the MPP may be desirable to avoid a stopping scenario in which you’d have to shed power past the MPP

## Slide 3: Experimental Method
Allow turbine to freewheel in recirculating flume
Bring turbine to critical TSR under torque control
Allow turbine to rotate until it ceases (stall event)
Repeat (many times)
Analyze conditions using turbine sensor data, classification algorithm, and PIV
6-axis load cells
Servo motor with encoder

## Slide 4: Characterizing a Stall Event
Notes: K-means: Method used to robustly identify modes of turbine operation
User specifies number of distinct clusters
Inputs are turbine rotational speed and acceleration
Assigns points into groups such that points are most similar to each other and most dissimilar from points in other groups
Number of groups, inputs, and degree of smoothing iterated to maximize distance between distinct groups
Five clusters ultimately identified for characterizing stall events

## Slide 5: Characterizing a Stall Event

## Slide 6: Characterizing a Stall Event
Notes: Increase legibility of legends, increase all font sizes

## Slide 7: Characterizing a Stall Event

## Slide 8: Characterizing a Stall Event

## Slide 9: Characterizing a Stall Event

## Slide 10: Characterizing a Stall Event

## Slide 11: Stall Event Statistics
n = 288
>
Notes: Change last bar to >60s

## Slide 12: Stall Event Statistics
n = 288
Notes: Fill bars, add phase averaged plot showing stall point identified

## Slide 13: PIV of Upstream Conditions during Stall Event

## Slide 14: Conclusions
When:
Where:
Why:
After range of time, empirical distribution
At the same angular position
Prolonged turbulent inflow speed deficit, loss of momentum
Notes: Stall events occur after a range of time that can be described by an empirical statistical distribution
Identified point at which turbine has stalled corresponds to same angular position for majority of iterations
Stall events likely occur due to hysteresis of turbine momentum: stall occurs after prolonged inflow speed deficit without turbulent gust at critical TSR

## Slide 15: Acknowledgements
Experiments conducted with the assistance of Danny Sale, Dominic Forbush, and Michelle Hickner of UW
Experiments conduced at Bamfield Marine Sciences Centre, Bamfield, BC
Funding from US DOE & NAVFAC
Questions?

## Slide 16: Bubble Visualization of Stall Event
Straight-bladed turbine, 2 blades