## Slide 1: Acoustic Characterization of Hydrokinetic Turbine
Brian Polagye & Paul Murphy
Department of Mechanical Engineering
University of Washington
September 9, 2015

## Slide 2
Study Overview
Characterize sound from a river current turbine
Free-drifting hydrophone measurements
  Minimize masking from flow noise
  Evaluate three hypotheses:
  The turbine will produce measureable sound
  Turbine sound characteristics will vary with turbine operating state
  Received levels will vary with spatial position on the river

## Slide 3
Study Motivation
Underwater sound produced by current turbines can affect marine animals
  Acoustic injury unlikely
  Behavioral modification possible
  Few studies of sound characteristics from current turbines, including temporal and spatial variations
Sockeye Salmon migration

## Slide 4
River Current Turbine
Ocean Renewable Power Company RivGen ®
Direct-Drive Generator
Four-bladed Helical Turbine
Notes: 11 m length, 1.4 m diameter, hub height of 2.5 m
Designed for community scale power – 15 kW at optimal TSR

## Slide 5
Study Location
Source: Google Earth
y
x
Iguigig, Alaska
Notes: 150 m wide, 5 m deep, average velocity ~ 2m/s 10-15% TI, cobbled bottom overlying unconsolidated sediments
Mode 1 cut-off of about 50 Hz

## Slide 6
Measurement System
1.15 m
Hydrophone: Loggerhead DSG
50 kHz recording rate
GPS: QStarz BT-Q1000eX
10 Hz recording rate
Met Station: Airmar PB200
1-2 Hz recording rate
Backup GPS
Spar attitude (heading, pitch, roll)
Surface Wave Instrumentation Float with Tracking (SWIFT)
Thomson, J. (2012). Wave breaking dissipation observed with “swift” drifters. Journal of Atmospheric and Oceanic Technology, 29(12), 1866-1882.

## Slide 7
Lagrangian Viewpoint

## Slide 8
Sources of Turbine Sound
Generator Tones
Misaligned Shaft Bearing
Blade Vibration
Upstream
Downstream

## Slide 9
Drift Location Uncertainty
Poor GPS accuracy for ~ 20% of drifts
  > 5 m separation between position recorded by GPS logger and met station GPS
  Limited number of satellites at high latitude
  Restricted sky view from river embankment
Notes: Had trouble even determining the location of the turbine (original estimate was off by 10 m) – brought a GPS-RTK system for field work this past summer.

## Slide 10
Sources of Contaminating Noise
Fishing Vessel Startup and Motoring Away
SWIFT Bobbing
(splash + flow-noise)
Manually review each drift and establish “quarantine zones”

## Slide 11
Dependence on Turbine State
Narrowband Spectra at Closest Point of Approach
Notes: Variations in frequency of primary tone

## Slide 12
Dependence on Turbine State?
Broadband Sound Pressure Level at Closest Point of Approach
Notes: Perhaps more subtle variations are present at specific frequencies, but not able to resolve broadband variations (at least with GPS accuracy)

## Slide 13
Spatial Extent of Drifts
SWIFT drifter and RivGen marker float
Notes: Plot is showing number of drifts accepted after QA/QC process: approximately 3:1 effort to data ratio – many replicates possible in relative short time, particularly running 3 SWIFTs at a time

## Slide 14
Spatial Variation in Turbine Sound
Optimal Power
Braked
RivGen
Notes: Relatively indistinct from background (except 100 Hz tone) at a range > 50 m

## Slide 15
Context for Turbine Operation
Turbine at optimal operating point with fishing vessel nearby

## Slide 16
Conclusions
Turbine produces sound at frequencies < 2 kHz
  Likely audible to fish across the width of river
  May have behavioral implications
  Acoustic measurements can provide useful environmental and technical information
  Drifting measurements useful, but challenges remain
  Measurements of sound at < 50 Hz
  Identification and removal of self-noise events

## Slide 17
Acknowledgements
Financial support for this project is generously provided by the US Department of Energy under FG36-08GO18179-M001.
Many thanks to Monty Worthington & Ryan Tyler (Ocean Renewable Power Company) for providing the study turbine, the village of Iguigig, Peter Dahl (University of Washington) for helpful discussions, and Alex de Klerk, Emma Cotter, & Joe Talbert (University of Washington) for field support.