## Slide 1: Measurement of Acoustic Pressure and Particle Acceleration Near a River Current Turbine to Assess Disturbances To Fishes
A Masters Defense
by
Paul Murphy
Marine Renewable Energy Lab | Applied Physics Lab

## Slide 2: Committee Members
Professor Peter H. Dahl
Mechanical Engineering and Applied Physics Lab
Professor Brian Polagye
Mechanical Engineering
Dr. David Dall’Osto
Applied Physics Lab

## Slide 3: Motivations

## Slide 4: Powering Remote Alaskan Communities
Energy costs are high in remote areas of Alaska
Diesel fuel must be shipped by cargo plane

## Slide 5: An Alternative Source of Power
Power from River Current Turbines may be an economically competitive alternative

## Slide 6: Possible Environmental Effects
Sound from turbines may affect fish
Physical harm is unlikely
Behavioral changes could result in change to the overall fish population

## Slide 7: Reliance on Fish Resource
Subsistence Based Riverine Communities
Commercial and Sport Fishing Industries
  State of Alaska monitors Salmon populations closely, and sets catch limits accordingly

## Slide 8: Sockeye Salmon (Oncorhynchus nerka)
Particle Motion (primary mode of sensation)
  Otolith (located in inner ear)
Pressure (secondary mode of sensation)
  Swim Bladder (not proximal to inner ear)

## Slide 9: Fish Hearing Sensitivity

## Slide 10: Particle Nature of Sound
[Animation courtesy of Dr. Dan Russell, Grad. Prog. Acoustics, Penn State]
Acoustic Particle – smallest volume of fluid with density equal to the mean fluid density.

## Slide 11: Objectives
Measure acoustic pressure and particle acceleration near an operating river current turbine
Secondarily, test a drifting hydrophone system capable of determining source bearing with a fixed hydrophone array

## Slide 12: Site and Measurement Methods

## Slide 13: Study Site: Igiugig Alaska

## Slide 14: Kviachak River, Lake Iliamna

## Slide 15: River Domain
Depth (d) < Width (w) < Length (L)
“Across-channel” (perpendicular to bulk flow)
“Along-channel” (parallel to bulk flow)
“Thalweg” – line of greatest depth
Depth variation in both across- and along-channel

## Slide 16: Site Characteristics
Current velocity often exceeds 2 m/s
Low turbidity, little debris (driftwood, etc), good visibility
Bottom: small cobble (D < 0.10 cm) over gravel, sand

## Slide 17: Turbine Site
Current
Direction
Upstream Moorings
Shore Station
RivGen

## Slide 18: RivGen (ORPC)

## Slide 19: River Turbine Sound Sources
Generator Vibration [rotation rate, gen. design]
  Expected frequency ~ 50 Hz and harmonics
Blade Vibration [blade structural modes]
Blade Passing Frame [rotation rate, # of blades]
  Expected frequency ~ 3-4 Hz and harmonics

## Slide 20: Unlikely Sound Sources
Turbulent Noise [Quadrapole]
Cavitation [Monopole]

## Slide 21: RivRaft Drifting Platform

## Slide 22: Benefits of Drifting Platforms
Drifting platforms reduce fluid motion over the face of hydrophones
This reduces “flow noise”, a type of pseudo sound that can mask propagating sound

## Slide 23: RivRaft Components

## Slide 24: Chandelier Design Considerations
Designed to measure both particle acceleration and estimate source bearing
Following damage to hydrophones: ad-hoc two hydrophone vertical array was built on site

## Slide 25: Measuring Particle Acceleration
Approximating the pressure gradient in the linearized Euler Eq.:

## Slide 26: Measuring Particle Acceleration
Hydrophone spacing d must satisfy d < λ/8 for acceptable error

## Slide 27: Measuring Particle Acceleration
Hydrophone separation of 20 cm for bandwidth up to 1000 Hz
Mean hydrophone depth of 50 cm

## Slide 28: RivRaft Instrumentation
Hydrophones: icListen HF
  10 - 200 kHz, -168 V/μPa
  Up to 512 kS/sec
  Perforated PVC shielding
  Master/Slave Synchronization

## Slide 29: RivRaft Instrumentation
ADV: Nortek Vector
  Internal IMU
GPS: QStarz Racing Pro
GoPro 3 Hero (x2)

## Slide 30: RivRaft Performance

## Slide 31: Raft Stability: Heading

## Slide 32: Raft Stability: Pitch and Roll
Measured by ADV probe at a depth of 50 cm

## Slide 33: Raft Stability: Relative Velocity
Measured by ADV probe at a depth of 50 cm

## Slide 34: Acoustic Measurements

## Slide 35: Measurement Log (Abridged)
8/14 – Arrived. Raft assembled.
8/18 – Damage to three hydrophones
8/25 – Five drifts with vertical 2-hydrophone array
  3 “Braked” (turbine stalled)
  2 “Optimal” (turbine at optimal power output)

## Slide 36: 8/14 - Assembling the Raft

## Slide 37: RivRaft Drift Paths

## Slide 38: RivRaft Drift Paths (8/25)
Flow Direction

## Slide 39: Ok, but what does it sound like?

## Slide 40: “Clicking” (Optimal 1)

## Slide 41: RivRaft Drift Paths
Flow Direction

## Slide 42: Braked 1 Pressure Spectrogram

## Slide 43: Optimal 1 Avg. Pressure Spectrogram

## Slide 44: Pressure Spectra

## Slide 45: Acceleration Spectra

## Slide 46: Tones at 100, 200, and 300 Hz
Harmonic structure with fundamental at 100 Hz.
For simplicity, they will be designated ‘H1’, ‘H2’, ‘H3’

## Slide 47: Optimal 1 Avg. Pressure Spectrogram

## Slide 48: ‘H1’ Frequency & RivGen Rotation Rate

## Slide 49: ‘H1’ arms (vertical) & RivGen Rotation Rate

## Slide 50: Possible Source of Tones
It is plausible that vibration from generator “cogging” is the source of the 100 Hz tone and harmonics
“Cogging” is caused by the periodic passing of magnetic poles and windings
Minimized by 3-phase designs, but still present

## Slide 51: Relevance to Sockeye Salmon Hearing
The 100 tone is within the estimated hearing frequency range of Atlantic Salmon
Level of 100 Hz tone is within the same order as behavioral threshold levels
It is not clear if any of the tones would be sensed by fishes at the ranges measured

## Slide 52: How does level vary with range?
r
Flow Direction

## Slide 53: Level of ‘H1’ Tone with Range

## Slide 54: Source Localization

## Slide 55: Source Localization: Theory

## Slide 56: Estimating Time Delay

## Slide 57: Estimating Time Delay

## Slide 58: Tracking the R.V. Robertson (no IMU)

## Slide 59: RivGen “Source” rel. to Vertical Array

## Slide 60: Challenges

## Slide 61: Logistical Constraints

## Slide 62: RivRaft Deployment

## Slide 63: RivRaft Deployment

## Slide 64: Summary of Findings

## Slide 65: Summary
Tonal peaks appear only during operation
  Fundamental and harmonics, approx. 100, 200, 300 Hz
Both frequency and level of the ‘H1’ (100 Hz) tone appear to vary with the rotation rate of the turbine
RMS level of the ‘H1’ tone decays to within 5 dB of ambient within 150 m of source

## Slide 66: Summary
Broadband “Clicking” Sound
  Operation only
Drifting platform is effective at reducing flow noise
  A light and compact design is beneficial

## Slide 67: Acknowledgements
The Applied Physics Lab, University of Washington
Joe Talbert, Alex de Klerk, Curtis Rusch
Mechanical Engineering, University of Washington
Brian Polagye and Emma Cotter
Ocean Renewable Power Company (ORPC)
Monty Worthington, Ryan Tyler, James Donegan

## Slide 68: Masters Committee
Professor Peter H. Dahl
Professor Brian Polagye
Dr. David Dall’Osto

## Slide 69
Additional thanks to members of
The Marine Renewable Energy Lab
and
The APL Underwater Acoustics Lab
for their support and guidance.

## Slide 70: Research Sponsors
The Northwest National Marine Renewable Energy Center (NNMREC)
Sustainability of Tidal Energy (STE)

## Slide 71: Questions