## Slide 2: Two Water Resource System Examples: Australia, and California
Stephen J. (Steve) Burges,
P.E., P.H., D.WRE.
Professor Emeritus
Department of Civil and Environmental Engineering
University of Washington
CEWA 578 – Lecture for Professor Jessica Lundquist, April 18, 2023

## Slide 3
Topics
Municipal Water Supply, Newcastle, Australia:
Chichester Dam, dam safety modifications
Water Supply in California:
Major dams, distribution network, infrastructure vulnerability – example Oroville Dam

## Slide 4
My early years – Newcastle Australia:

## Slide 5
Born, Newcastle, 1944

## Slide 6
0.5 miles
Newcastle
Coal Storage Yards
South Channel Hunter River
Hunter River

## Slide 7
University of Newcastle 1962 - 1966
199 degrees granted in 1966
Hunter Dist. Water Board
0.5 miles

## Slide 8
Summer internships – trainee civil engineer, Hunter District Water Board 1963 - 66:
Member of construction crews – sewers, water supply, treatment plants, pumping stations.
I gained huge respect for workers who do hard physical work.
Engineers must not waste any worker’s time!

## Slide 9
Post- baccalaureate Construction Engineering Experience
Hunter District Water Board – (now, Hunter Water)
Nov 1966 - August 1967

## Slide 10
Topics
Municipal Water Supply, Newcastle, Australia:
Chichester Dam, dam safety modifications
Water Supply in California:
Major dams, distribution network, infrastructure vulnerability – example Oroville Dam

## Slide 11
Life-cycle issues in civil engineering infrastructure
Lowering spillway, Chichester Dam

## Slide 12
Chichester Dam was constructed between 1915 and 1926 as the Hunter Valley’s first dedicated drinking water storage system.
Chichester Dam is one of the Hunter’s most important freshwater storage facilities contributing about 35 per cent of the Lower Hunter’s potable water supply.
The catchment for Chichester Dam is largely within the Barrington Tops National Park, which is a declared wilderness area. As a result, it is one of the most pristine catchments in Australia with large areas unaffected by human activity
https://www.hunterwater.com.au/Water-and-Sewer/Water-Supply/Dams-and-Catchments/Chichester-Dam.aspx

## Slide 15
~ 62 road miles
Pipeline route and supply region

## Slide 16
Spillway
Dam

## Slide 17
Dam constructed 1917-1927
Photo 1925 – reservoir filling
Wall height ~ 140 ft.
Spillway crest ~ 120 ft.
Active Storage 14,900 Ac. Ft.

## Slide 18
Wall length ~ 550 ft.
safety fence
280 ft. long “ogee” spillway
Top radius of curvature ~ 1200 ft.

## Slide 19
Sharp crested weir - free “Nappe”
Ogee design emulates the free nappe to avoid negative pressures at water - weir interface
See pages 365-376 - U.S. Bureau of Reclamation, Design of Small Dams, Third Edition, Denver, Colorado, 1987, for details of discharge over an uncontrolled Ogee Crest
Pressure is atmospheric

## Slide 20
Looking downstream showing low-cost “coffer dam” and river bypass channel and scour pipes
Excavated bedrock
Coffer dam
Bypass channel
Scour pipes

## Slide 21
Looking upstream showing construction progress - coffer dam, river bypass channel and scour pipes
Bypass channel
Scour pipes
Work area access

## Slide 22
View – 1919 ‘cyclopean’ system of interlocking concrete blocks and large boulders, each approximately 300 cubic yards – effective water blocking construction
Scour pipes

## Slide 23
Scour pipes – flow bypass
Pipeline Feeder
Cableway

## Slide 24
Dam serving as coffer dam

## Slide 25
Cableways
Spillway under construction

## Slide 26
Lower spillway required for a larger flood - loss of water storage capacity
Max water level for spillway design flood
Dam safety – spillway must discharge largest flood – PMF – without overtopping dam wall

## Slide 28
10.00 | 28,334 | 34,532 | 27,449 |  | 
10.70 | 31,361 | 38,221 | 30,381 | Original Spillway _ Max Water depth | 
11.00 | 32,689 | 39,839 | 31,667 | Spillway modeled as broad crest | 
11.70 | 35,858 | 43,702 | 34,737 |  | 
12.70 | 40,552 | 49,423 | 39,285 | Spilway lowered 2 ft. 1967 | 
13.00 | 41,997 | 51,184 | 40,685 |  | 
14.00 | 46,935 | 57,202 | 45,469 |  | 
15.00 | 52,053 | 63,439 | 50,426 |  | 
16.00 | 57,344 | 69,888 | 55,552 |  | 
17.00 | 62,803 | 76,541 | 60,841 |  | 
17.70 | 66,722 | 81,317 | 64,637 | Spillway lowered 9 ft. | 
 |  |  | Spillway Flow Rate |  | 
 |  | cfs |  | cms | 
Original Peak Flow |  | 32,000 | Original | 900 | 
Capacity after lowering |  | 39,290 | Lowered 2 Ft | 1,113 | 
 |  | 64,640 | Lowered (2 + 7) Ft | 1,830 | 
1984 Estimated PMF |  |  |  | 2,400 | 

## Slide 29
Flow over original spillway

## Slide 30
Pipeline – 36 inch dia. -
gravity flow – mainly above ground
Minimum head 430 ft.
Receiving reservoirs El.
192 ft. and 301 ft.
9 miles wood-stave
53 miles - U.S. supplied rolled steel, fabricated in Newcastle

## Slide 31
Wood stave pipeline construction
Steel hoop rings

## Slide 32
Wood-stave pipeline

## Slide 33
Wood-stave pipeline
Support piers
Support cradles
Pipeline river crossing

## Slide 34
Steel pipeline construction
Pipe seams - welded

## Slide 35
Portion of original steel pipeline – note joints
Steel pipe joint “steel bands” – lead seal

## Slide 36
Pouring molten lead seal

## Slide 37
Modern steel pipeline
0.1 miles

## Slide 38
Major Pipeline Systems – Complex Infrastructure
See e.g.
https://en.wikipedia.org/wiki/Trans-Alaska_Pipeline_System
Water System Design Manual
https://doh.wa.gov/sites/default/files/2022-02/331-123.pdf?ver=2019-10-03-153237-220
Pipeline design and maintenance:
Right of way, ground conditions, river crossings
Seismic
Structural integrity
Materials (corrosion and wear)
Thermal influences (expansion and contraction)
Access, air relief valves, shutoff valves, drainage valves
Physical, chemical, and biological security
Cyber security
Ongoing O & M and replacement

## Slide 39
Major Dam Safety Upgrades – Chichester Dam
1967: spillway lowered by 2 feet and later by an additional 7 feet to increase flood capacity
1985: spillway relocated to center of the dam wall and returned to original height; dam post-tensioned with 93 cables.
1995: seepage potential reduced under the northern abutment
2003: improved drainage system for foundations installed and the left parapet wall raised to prevent overtopping in major flood.
Hunter Water S170 Register - SHI No 3630116; Name Chichester Dam.pdf

## Slide 40
Major Dam Safety Upgrades – Chichester Dam
The NSW Government formed a regulator called the ‘Dams Safety Committee’(DSC) in 1976 and charged them with determining a set of rules for dam safety based on the concept of a dam’s site specific ‘Consequence Category’.
Chichester was its first case.
Original spillway capacity was about 900 m3/sec.
The 1984 PMF was determined at 2,400 m3/sec.
Post tensioning (P/T) and relocation of spillway to meet new PMF
Notes from Jeff Gleeson, Hunter Water, August 2017

## Slide 41
Major Dam Safety Upgrades – Chichester Dam
From 1984 to 2017 the PMF has risen progressively from 2,400 m3/sec to 5,900 m3/sec.
Rated spillway capacity 3,300 m3/sec.
Conservative design worked to about 3,600 m3/sec.
P/T tendons had to be checked frequently.
The dam is “deficient” 2017 -.
Dams Safety Regulation 2019 – NSW Government
Annual reports from dam owner/operators required
https://legislation.nsw.gov.au/view/html/inforce/current/sl-2019-0506
Notes from Jeff Gleeson, Hunter Water, August 2017 – Updated with Dam Safety Report, April 2023, Steve Burges

## Slide 43
Report for December 31, 2021

## Slide 44
- Davis, 1942

## Slide 46
- Davis, 1942

## Slide 50
Failure Modes
Overturning
Sliding
Pivot

## Slide 51
Failure Modes
Overturning
Sliding
Structural
Dam has to be safe for highest flow rate - PMF
Subsurface erosion

## Slide 52
Major Dam Safety Upgrades
1967: spillway lowered by 2 feet (Steve Burges site engineer) and later by an additional 7 feet to increase flood capacity.

## Slide 53
Activities (site engineer) - Preparation for Chichester Dam Spillway lowering - Dec 1966:
Study “SAA Explosives Code” and train a “shot firer”
Plan all site safety and construction logistics
Design a safety fence and arrange for fabrication
Develop a blasting pattern and schedule.

## Slide 54
Site engineer - Jan 1967 – Mar 1967
Use explosives (gelignite) to remove top 2 feet of spillway

## Slide 55
Highest priority - safety for all crew and site visitors
Have materials and equipment ready for the crew – logistics!
I welcomed and used inputs from every crew member – mostly former under-ground coal miners
We developed drill and blast patterns after 1 week of trials -- one blast pattern per day

## Slide 56
Safety fence - no design standards available
Work barge
Air compressor
March 1967

## Slide 57
Major Dam Safety Upgrades
1967: spillway lowered by 2 feet and later by an additional 7 feet to increase flood capacity
1985: spillway relocated to center of the dam wall and returned to original height, dam post-tensioned with 93 cables.
The upgraded actions were made to minimize the possibility of water overtopping the main dam wall and against rotational failure.

## Slide 58
Post Tensioning Cable Schematic

## Slide 59
Post Tensioning Cable Locations - Spillway

## Slide 60
Post Tensioning Cable Placement
Anchor length
8 to 9 m

## Slide 61
Post Tensioning Cable Inspection

## Slide 62
Post Tensioning Testing

## Slide 63
Summary of P/T tendon “restressing” 2005 - 2015
Notes from Jeff Gleeson, Hunter Water, August 2017

## Slide 64
Notes from Jeff Gleeson, Hunter Water, August 2017
Figure B1 - % UTS (Ultimate Tensile Strength) Comparison of results for 2015 to 2005

## Slide 65
Photo - Futurepast Heritage Consulting Pty Ltd June 8, 2010

## Slide 66
Photo - Futurepast Heritage Consulting Pty Ltd June 8, 2010
Hydraulic Jump Forming Structures
Competent Bedrock

## Slide 67
485 ft. long “ogee” spillway
Photo - Futurepast Heritage Consulting Pty Ltd June 8, 2010
Major design consideration: preventing cavitation damage

## Slide 68
Hydraulic model – 1:48 scale for replacement spillway design
Froude number scaling - 1967-1968
Futurepast Heritage Consulting Pty Ltd May 19, 2010
Spillway scaled for 485 ft. prototype
Multi-level water intake ports

## Slide 69
Hydraulic model
=
2 cfs model ~ 32,000 cfs,
~ 900 cms
Futurepast Heritage Consulting Pty Ltd May 19, 2010

## Slide 71
Summary Observations
Engineering designs are made under uncertainty.
Supplies and labor availability have major influences on construction – World War I was a major disruption of the Chichester Dam and pipeline project.
Knowledge and observations gained with time may necessitate modification to design and operation of facilities; the economic life of infrastructure is ~40 yrs.
The changes to Chichester Dam and spillway occurred over three or more professional lifetimes. It is essential that Institutional Memory is retained.

## Slide 72
Topics
Municipal Water Supply, Newcastle, Australia:
Chichester Dam, dam safety modifications
Water Supply in California:
Major dams, distribution network, infrastructure vulnerability – example Oroville Dam

## Slide 73
Major reservoirs in California and distribution system

## Slide 74
https://en.wikipedia.org/wiki/List_of_largest_reservoirs_of_California#/media/File:Water_in_California_new.png
Map of California's interconnected water system, including all eleven reservoirs over 1 million acre feet (1.2 km3) and selected smaller ones (Wikipedia)
80 miles

## Slide 75
4.55 MAF, 1945
2.45 MAF, 1962
1.12 MAF, 1956
2.40 MAF, 1979
3.54 MAF, 1968
2.04 MAF, 1979

## Slide 76
32 MAF, 1935-36, Actual 26.1 MAF
Los Angeles imports

## Slide 77
Combined use of stored surface water and ground water
Cyclic storage:
multi - year to decadal time scales for aquifer recharge and pumping
D.P. Lettenmaier and S.J. Burges, "Cyclic Storage: A Preliminary Assessment," Groundwater, Vol. 20, No. 3, 278-288, 1982.

## Slide 78
Use of ground water to mitigate against drought
Ground water reservoirs have known supply; there is considerable uncertainty about supply from surface reservoirs leading up to, and during drought
What is the time history of ground water use?

## Slide 79
113
145
118
182
259
341
145 cubic km = 117.6 MAF = 7.8 yr. crf.
Mean ann. flow Colorado R. = 15 MAF
Leonard F. Konikow, Groundwater Depletion in the United States (1900−2008), USGS Scientific Investigations Report 2013−5079

## Slide 80
We must not abuse our ground water resources!

## Slide 81
California State Water Project – importance of Oroville Dam

## Slide 82
The Sacramento River HR is the main water supply for much of California’s urban and agricultural areas.
Annual runoff in the HR averages about 22.4 maf, which is nearly one-third of the State’s total natural runoff. Major water supplies in the region are provided through surface storage reservoirs.
The two largest surface water projects in the region are USBR’s Shasta Lake (Central Valley Project) on the upper Sacramento River and Lake Oroville (DWR’s State Water Project) on the Feather River.

## Slide 83
In all, there are more than 40 major surface water reservoirs in the region. Municipal, industrial, and agricultural supplies to the region are about 8 maf, with groundwater providing about 2.5 maf of that total.
Much of the remainder of the runoff goes to dedicated natural flows, which support various environmental requirements, including
in-stream fishery flows and flushing flows in the Delta.

## Slide 84
4.55 MAF, 1945
2.45 MAF, 1962
1.12 MAF, 1956
2.40 MAF, 1979
3.54 MAF, 1968
2.04 MAF, 1979
Natural mean annual runoff – Sacramento R. = 22.4 MAF
Storage ratio > (2.45 + 4.55 + 3.54)/22.4 = 0.47

## Slide 85
Sacramento River annual flow variability
Tree-ring index reconstructions

## Slide 86
http://www.water.ca.gov/waterconditions/docs/tree_ring_report_for_web.pdf

## Slide 89
Oroville Dam – Importance to California State Water Project
Dam safety issues – 2017

## Slide 90
http://www.water.ca.gov/maps/state.cfm
Oroville Dam

## Slide 91
All water projects and rivers (blue)

## Slide 92
Features of Oroville Dam

## Slide 93
Cross-section earth-fill Oroville Dam

## Slide 94
Failure mechanisms for an earth-fill dam
Reservoir overtopping and erosion of downstream face
Multiple causes - erosion and slumping of upstream face

## Slide 95
Failure mechanisms for an earth-fill dam
“Piping” or seepage flow and erosion of downstream face

## Slide 96
Failure mechanisms for an earth-fill dam
Structural instability and slumping – seismic - overtopping and erosion of downstream face

## Slide 97
Failure mechanisms for an earth-fill dam
“Piping” or seepage flow failure preventative measures

## Slide 98
https://www.youtube.com/watch?v=Qp-YxXlMnlg&ab_channel=MillieKay
Seepage flow path failure preventative measures

## Slide 99
March 2017
Hydro power plant not at risk
Could the main earth dam have failed?
Relatively flat part of 3000 ft. long chute spillway
Damaged spillway and major erosion path

## Slide 100
Main zoned-earth dam
~ 80 million cubic yards
Height 770 ft.
Highest in USA - 1968
Emergency spillway flow starts at El. 901 Ft.
Crest elevation – 922 Ft.
June 7, 2013

## Slide 101
Upstream rip-rap wave protection
June 7, 2013

## Slide 102
June 7, 2013
Normal spillway flow (roll waves)
Energy dissipaters
Channel width 179 ft.

## Slide 103
Feb 27, 2017
https://en.wikipedia.org/wiki/Oroville_Dam#/media/File:Oroville_Dam_spillway_damage_27_Feb_2017.jpg

## Slide 104
Reservoir: I – O = dS/dT
Main spillway for controlled reservoir release
Earth dam – 6,920 ft. long
Hydro power plant
March 2017

## Slide 105
Emergency spillway -1,730 ft. long - for uncontrolled release of floods up to PMF: 800 ft “broad crest weir” + 930 ft “ogee.”
March 2017

## Slide 106
Normal operation:
Releases from power plant and from a “bypass valve” for environmental flows (and power production)
When reservoir at spillway level, releases from power plant and spillway gates as appropriate.
Extreme flood conditions:
Release from controlled spillway and emergency spillway; hydro plant may be inoperable.

## Slide 107
http://www.smartbrief.com/s/2017/03/oroville-dam-spillway-repair-may-require-temporary-solution
Release through spillway control gates
Spillway gates
March, 2017

## Slide 108
June 7, 2013
Emergency spillway
Note location similarity to Englewood Dam (1922) emergency spillway, Miami Conservancy District, Ohio
Major difference – greater erosional potential at Oroville: longer hillside runout length to river. Runout domain rock stability critical to safe performance
Ogee section
Broad crest weir

## Slide 109
Outlet works
Emergency spillway
Englewood Dam, Ohio – completed 1922
0.1 miles

## Slide 110
Emergency Spillway
Existing rock with shallow soil cover
Overflow path
May 1984

## Slide 111
Outflow armoring
Top of dam

## Slide 112
Engineered wing walls
May 1984
Spillway overflow path

## Slide 113
June 7, 2013
Oroville Emergency spillway
Flow path

## Slide 114
Water overflowed the parking lot past the emergency spillway (in the background), while water continued to flow through the main spillway (in the foreground), on February 11, 2017.
https://en.wikipedia.org/wiki/Oroville_Dam#/media/File:Oroville_dam_spillover_2017-02-11.jpg
Parking lot

## Slide 115
Water from the Oroville Dam flows over the Emergency Spillway at Lake Oroville on Sunday February 12, 2017.
https://en.wikipedia.org/wiki/Oroville_Dam#/media/File:Oroville_Emergency_Spillway_Carrying_Water.jpg

## Slide 117
Back cutting at 10 ft/hour

## Slide 118
Repair schedule:
March 17, 2017, report of Board of Consultants
Work scheduled July – October 2017
https://ferc.gov/sites/default/files/2020-04/03-17-17Orovilledam.pdf

## Slide 119
Repair schedule (ctd):
The presented design criteria for spillway flows are as follows:
Restore both spillways to pass the Probable Maximum Flood (PMF) flows (646,000 cfs) without failing, and with damage below the Emergency Spillway to be expected.
These include the following estimated flows:
 Gated Spillway peak design outflow of 277,000 cfs
Emergency Spillway peak design outflow of 369,000 cfs (estimated - sjb - 16.0 to 16.6 ft water depth at spillway)

## Slide 120
Repair schedule (ctd):
Operational maximum release goals are as follows:
 Operate the reservoir to limit the Gated Spillway maximum design release to 100,000 cfs
 Operate the reservoir to prevent spill over the Emergency Spillway.
It is the BOC’s understanding that peak outflows through the Gated Spillway will be limited to about 150,000 cfs, which is consistent with historic peak releases, and are designed to prevent overtopping of levees and flooding of communities downstream of the dam.

## Slide 122
Reconstructed lower chute spillway Nov. 17, 2017

## Slide 123
April 14, 2015
Emergency Spillway and overflow region before use

## Slide 124
May 18, 2017
Emergency Spillway and overflow region after erosion damage

## Slide 125
Sep 21, 2020
Emergency Spillway overflow region after extensive repair

## Slide 126
DWR Contract to Kiewitt to rebuild spillway $275 Million
Actual cost approx. $500 Million
Revised cost approx. $870 Million – Jan 26, 2018
Start
End

## Slide 127
Oroville Dam, CA, failed spillway, Feb 27, 2017
https://en.wikipedia.org/wiki/Oroville_Dam#/media/File:Oroville_Dam_spillway_damage_27_Feb_2017.jpg
Cost of replacement of spillway 2017-2018 and stabilization below emergency spillway – 2018, $1.2B (DWR Feb. 2021)
FEMA pays $630 Million

## Slide 128
Two Oroville Spillway webinars:
Physical Aspects of the Oroville Dam Incident
https://www.youtube.com/watch?v=3JygTm8iiWQ
March 5, 2018, 2:00 PM EST
John W. France, PE, D.GE, D.WRE; Vice President, AECOM, Independent Forensic Team Leader
Lessons for Dam Safety from the Oroville Dam Incident
https://www.youtube.com/watch?v=YjgugkIfwWQ
March 14, 2018, 2:00 PM EST
Stephen J. Rigbey, Director Dam Safety at BC Hydro, Independent Forensic Team member

## Slide 131
Questions?

## Slide 132
Extras

## Slide 133
Images of Oroville Dam March 2017
Source:
https://www.bing.com/images/search?q=oroville+dam+spillway&qpvt=oroville+dam+spillway&qpvt=oroville+dam+spillway&qpvt=oroville+dam+spillway&FORM=IGRE

## Slide 134
Tolerable Risk Resources – US Army Corps of Engineers
https://www.rmc.usace.army.mil/Reference-Center/Tolerable-Risk/
1. FEMA
https://www.fema.gov/emergency-managers/risk-management/dam-safety/federal-guidelines
2. COE
U.S. Army Corps of Engineers (USACE) Dam Safety Policy and Procedures
https://www.publications.usace.army.mil/Portals/76/Publications/EngineerRegulations/er_1110-2-1156.pdf
(528 pages) – See particularly “Chapter 10. Dam safety Risk Communication”
Rationale Behind the U.S. Army Corps of Engineers Tolerable Risk Guidelines
Check all four Listings under “Tolerable Risk References
3. US EPA
Risk communication in Action - The Tools of Message Mapping, US EPA625R-06012, 200.pdf (51 pages)

## Slide 135
Example of engineering failure due to lack of full knowledge of situation
Hunter District Water Board pipeline crossing of the South Channel Hunter River, 1965
Pressure test of fully charged new water pipeline
Blank flange failed during test
Faulty flange provided by an engineer from HDWB
What do you think happened?

## Slide 136
200 Feet
Hunter Water Pipeline – Crossing South Channel Hunter River
12/10/2006
Rectangular reinforced concrete portal frame supports damaged in 1965 during pipeline pressure “proof” test – created major repair problem

## Slide 137
200 Feet
Hunter Water Pipeline – Crossing South Channel Hunter River
12/10/2006
Blank flanges installed isolating this section of pipeline

## Slide 138
Example of tragic engineering failure due to negligence
Kansas City Hyatt Regency walkway collapse, July 17, 1981
114 people killed, 216 injured
https://en.wikipedia.org/wiki/Hyatt_Regency_walkway_collapse#:~:text=On%20July%2017%2C%201981%2C%20the,killing%20114%20and%20injuring%20216.

## Slide 144
March, 2017

## Slide 145
March, 2017

## Slide 146
March, 2017

## Slide 147
March, 2017

## Slide 148
March, 2017

## Slide 149
Feb 27, 2017
https://en.wikipedia.org/wiki/Oroville_Dam#/media/File:Oroville_Dam_spillway_damage_27_Feb_2017.jpg

## Slide 150
June 7, 2013
Emergency spillway

## Slide 151
Tolerable Risk Resources – US Army Corps of Engineers
https://www.rmc.usace.army.mil/Reference-Center/Tolerable-Risk/
1. FEMA
https://www.fema.gov/emergency-managers/risk-management/dam-safety/federal-guidelines
2. COE
U.S. Army Corps of Engineers (USACE) Dam Safety Policy and Procedures
https://www.publications.usace.army.mil/Portals/76/Publications/EngineerRegulations/er_1110-2-1156.pdf
(528 pages) – See particularly “Chapter 10. Dam safety Risk Communication”
Rationale Behind the U.S. Army Corps of Engineers Tolerable Risk Guidelines
Check all four Listings under “Tolerable Risk References
3. US EPA
Risk communication in Action - The Tools of Message Mapping, US EPA625R-06012, 200.pdf (51 pages)

## Slide 153
https://www.hunterwater.com.au/about-us/publications/annual-report

## Slide 158
Lake Oroville, the Oroville Dam, Thermalito Forebay and Thermalito Afterbay - Pumped Storage System
1 mile

## Slide 159
1 mile
Lake Oroville, the Oroville Dam, Thermalito Forebay and Thermalito Afterbay - Pumped Storage System

## Slide 160
DESIGN EVOLUTION OF OROVILLE DAM 1956-68
J. David Rogers, Ph.D., P.E., P.G., F.ASCE, F.GSA
Professor & Karl F. Hasselmann Chair in Geological Engineering
Missouri University of Science & Technology
2017 AEG Annual Meeting, Colorado Springs
https://www.aegweb.org/assets/docs/1-Rogers_-_AEG_TS7-Oroville_.pdf

## Slide 161
Orange County Ground Water Recharge Volume
Final expansion complete on world’s largest water reuse facility - Water Finance & Management - 4-17-2023.pdf
Volume = 130 mgd
Volume = 400 Acre Feet per day
Annual Volume = 146,000 Acre feet