## Slide 1
Hydrologic Models – Classification:
Lumped, Distributed - Conceptual to
Physically Based
Stephen J. (Steve) Burges
Professor Emeritus
Department of Civil and Environmental Engineering
University of Washington
Guest Lecture CEE 574 – Advanced Hydrology
April 20, 2016 – Updated July 5, 2024
Numerous Slides Provided by Professor Stephanie Kampf,
Colorado State University

## Slide 2
Topics:
Model Definitions and Modeling the water budget
Calibrating and testing a conceptual model using error free data
Calibration and test of a sophisticated soil physics based model and demonstration of the importance of accurate, bias-free measurements
Modeling a small watershed
Suggestions for a way forward

## Slide 3
Topics:
Model Definitions and Modeling the water budget

## Slide 4
Model calculations
Input
Output
Time
Precipitation
Time
Stream flow
Mathematical model = behavior of the system is represented by a set of equations, perhaps together with logical statements, expressing relationships between variables and parameters.
Clarke (1973) definition:

## Slide 5
Variable = Value changes over time; input or output
Parameter = Values may be modified for model calibration; typically constant over time
Variables and Parameters: internal or external factors that
(i) affect the rate at which water enters or leaves the model domain, or
(ii) represent characteristics of the material in the model domain that affect water movement
Domain = space represented in a mathematical model
Calibration = adjusting model parameters so that model output matches observations
Time
Stream flow
Observation data

## Slide 6
1D
2D
3D
x
x
y
x
y
z
x
x
y
x
y
z
How do we represent space in a model?

## Slide 7
Lumped model = Takes no account of the spatial distribution of input variables or parameters. Treats the domain as if it were homogeneous and subject to uniform rainfall.
Geometrically-distributed model = Describes spatial variability of input variables or parameters in terms of the geometric orientation of points in the model domain.
Model representations of space
1D
2D,
3D
Transitional:
Aggregated lumped models
Clarke (1973) definitions

## Slide 8: Lumped models
Do not account for the spatial distribution of input variables or parameters
Precipitation
Stream flow
Spatially averaged (1D) model calculations

## Slide 9: Aggregated lumped models
Can account for the spatial distribution of input variables or parameters.
Stream flow
Separate 1D calculations for each sub-domain
Precipitation

## Slide 10
1D (lumped) conceptual model:
Sacramento Model (SMA), 1973
Figure 2, Burnash et al., 1973
Water input
Land processes
“Outflow”
E T

## Slide 11
1D (lumped) conceptual model:
Sacramento Model (SMA), 1973
Figure 2, Burnash et al., 1973
16 model parameters
Major challenge for optimization algorithms

## Slide 12
Rainfall-runoff modeling
Choose model
Define the catchment boundaries
– subsurface not well defined
Select input time series
– precipitation, potential evapotranspiration
Determine suitable model parameters
– usually by forcing the predicted streamflow
time series to match the observed time series

## Slide 13
Crawford and Linsley (SWM IV) and Burnash et al (SMA) recognized the importance of representing basin precipitation correctly.
“Definition of basin precipitation is a complex problem that has not been resolved for areas
where precipitation reports are sparse.
Such areas constitute a major portion of the world and impose a genuine restriction on our ability to evaluate streamflow synthesis”.
Burnash et al, 1973

## Slide 14
Earliest example - US

## Slide 15
1D (lumped) model example:
Stanford Watershed Model (1960, 1966)
Figure 12-1, Linsley et al., 1982

## Slide 16
N. H. Crawford and R. K. Linsley, Stanford Watershed Model IV, 1966
Manual calibration

## Slide 17
N. H. Crawford and R. K. Linsley, Stanford Watershed Model IV, 1966
Remarkable achievement at the time

## Slide 18
Test the model with an independent input series
compare predicted with measured streamflow
(see, e.g., James and Burges, 1982)
Usually employ parameter optimization scheme
More recently, incorporate model, data, and parameter uncertainty
to produce probability distributions of
predicted streamflow time series

## Slide 19
Example:
Feyen, Vrugt, et. al., Journal of Hydrology 2007
Figure 11
LISFLOOD model

## Slide 20
daily discharge
Two years
Modeled - Observed

## Slide 21
Observed
Predicted` plus parameter uncertainty
Modeled - Observed
parameter uncertainty

## Slide 22
Modeled - Observed
Model and measurement uncertainty

## Slide 23
Desirable to produce smallest spread possible

## Slide 24
Test the model with an independent input series and compare with measured streamflow
Usually employ parameter optimization scheme
More recently, incorporate model, data, and parameter uncertainty
to produce probability distributions of
predicted streamflow time series
This approach is limited by:
uncertainties in subsurface boundary location
and errors and biases in input time series and
measured streamflow

## Slide 25
Topics:
Model Definitions and Modeling the water budget
Calibrating and testing a conceptual model using error free data

## Slide 26
Conceptual model – hillslope scale – mid 1980s
How useful are calibrated conceptual hydrological models for representing major floods?
Gan and Burges, WRR 1990 – (NSF supported)

## Slide 27
Sophisticated soil physics model of flow from prismatic homogeneous hillslopes
provided “error free” hydrologic signals
Operational model was calibrated by matching the modeled and “measured” outflow hydrograph time series
Calibrated conceptual Sacramento model - SMA (National Weather Service) used to predict hydrologic response to large rainfall

## Slide 28
Sacramento Model (SMA)
Figure 2, Burnash et al., 1973

## Slide 29
Case 1. 0.8 m deep Ksat = 2 cm/hr
Case 2. 1.6 m deep Ksat = 20 cm/hr
length 100 m
slope = 0.10

## Slide 30
0
130
.02
0.0
-.008
Oct Apr Oct Apr Oct
Time (months)
S-H Flow, cmsd
S-H - SMA, cmsd
.16
.12
.08
.04
0
Rain, mm/hr
Case 1: Ksat = 2 cm/hr soil 0.8 m deep
True minus Calibrated model
Rain
True flow rate
Runoff:
88% Surface flow
- Best calibration
Two Years

## Slide 31
0
130
.03
0.0
-.013
Oct Apr Oct Apr Oct
Time (months)
S-H Flow, cmsd
S-H - SMA, cmsd
.08
.06
.04
.02
0
Rain, mm/hr
Case 2: Ksat = 20 cm/hr soil 1.6 m deep - Best calibration
Runoff:
7% Surface flow
True flow rate
True minus Calibrated model

## Slide 32
0
130
.03
0.0
-.013
Oct Apr Oct Apr Oct
Time (months)
S-H Flow, cmsd
S-H - SMA, cmsd
.08
.06
.04
.02
0
Rain, mm/hr
Non-zero residuals result from inadequacies in model and errors in optimally estimated parameters

## Slide 33
Predicted hillslope hydrograph for 6-hour duration “probable maximum rainfall”
Extreme rain applied when:
hillslope relatively “wet”
hillslope relatively “dry”

## Slide 34
Case 1: Ksat = 2 cm/hr soil 0.8 m deep
“dry”
Hillslope condition at start of storm
“wet”
Extreme Flood hydrographs – “probable maximum flood”

## Slide 35
Case 1: Ksat = 2 cm/hr soil 0.8 m deep
“dry”
Hillslope condition at start of storm
“wet”
true
Calibrated model prediction
true
Calibrated model prediction
Calibrated model appears to be satisfactory for modeling extreme rainfall

## Slide 36
Case 2: Ksat = 20 cm/hr soil 1.6 m deep
“dry”
Hillslope condition at start of storm
“wet”
true
Calibrated model prediction
true
Calibrated model prediction
Calibrated model is unsatisfactory

## Slide 37
Summary:
Calibrated conceptual model using complete and “error free” inputs was unable to represent all flow processes.
Conceptual model does not provide spatial soil moisture patterns.
More complete hydrological representation needed.

## Slide 38
Topics:
Model Definitions and Modeling the water budget
Calibrating and testing a conceptual model using error free data
Calibration and test of a sophisticated soil physics based model and demonstration of the importance of accurate, bias-free measurements

## Slide 39: Measurements in space: Points
Surface
Subsurface
Unsaturated
Saturated
Channel

## Slide 40: Models: ‘fill in’ unknowns
In space
And in time
Time
Model time series
Surface
Unsaturated
Saturated
Channel

## Slide 41
Physically-based models:
Use conservation equations (mass, energy, and/or momentum)
In this case: Models solve the governing form of conservation equations (Partial Differential Equations - PDE’s)
St. Venant equations:
Conservation of mass and momentum
Richards’ (Darcy) equation:
Conservation of mass and momentum
Surface
Unsaturated
Saturated
Channel

## Slide 42
Link?
Measurement points
‘Continuous’ model
Insufficient data
Field heterogeneity
Measurement
Uncertainties
Scale discrepancies
Model uncertainties
structure
parameters
boundary conditions
initial conditions
Problems
often cited,
rarely addressed,
Not solved!

## Slide 43
Getting the right answers for the right reasons:
Linking measurements, analyses, and models to advance the science of hydrology
Kirchner, J.W., March 2006, Water Resources Research
“Scientific progress will mostly be achieved through the collision of theory and data, rather than through increasingly elaborate and parameter-rich models that may succeed as mathematical marionettes, dancing to match the calibration data even if their underlying premises are unrealistic.”

## Slide 44: Framework of knowns/unknowns:
Domain: Size and boundary conditions
Characteristics: surface and subsurface
Input: Precipitation
Output: surface and subsurface
Internal states and fluxes: surface and subsurface, including initial conditions

## Slide 45
Data from University of Washington site
Spatial hydrologic Model – Hydrus – 2D (Šimùnek, Sejna, van Genuchten, 1999)
Solves Richards’ equation for a variably saturated flow domain
Finite element solution scheme
Part of Professor Stephanie Kampf’s doctoral dissertation (2006); Kampf and Burges wrr, 2007, J. Hydrology, 2010 (NSF supported)

## Slide 46
University of Washington
Experimental Plots Constructed 1994

## Slide 47
Plot 1
Weather Stations
Summer 2005

## Slide 48
Experimental plot
Till-based soil:
33% gravel;
45% sand;
17% silt;
5% clay
Construction details
Kolsti et al (1995)
5 Piezometers

## Slide 49
Outflow
Tipping buckets

## Slide 50
Plot boundary conditions are known
Flow produced is subsurface for all cases shown

## Slide 51
Calibration piezometer
5

## Slide 52
Impermeable boundary
Boundary Conditions

## Slide 53
Controlled Experiment - Draining from saturation:
Irrigate to saturation
Turn off water supply
Measure outflow hydrograph and soil moisture state
July, 2005 and October, 2005, (known initial conditions)

## Slide 54
Controlled Experiment - Draining from saturation:
Model calibration objective:
Determine soil hydraulic characteristic curves for assumed homogeneous soil

## Slide 55
Calibration: inverse simulations - Hydrus2D
Calibration criteria: combinations of measured
subsurface flow hydrograph,
cumulative subsurface flow,
Soil water contents,
saturated water levels.

## Slide 56: Subsurface governing PDE
Change in water content over time
Sources and sinks
Unsaturated hydraulic conductivity function
Change in head over space
2D Richards’ equation, matrix flow

## Slide 57: Equations for water retention functions van Genuchten (1980)
Variable
for h < hs
θ = θs for h ≥ hs
θr = residual water content
θs = saturated water content
Ks = saturated hydraulic conductivity
l = 0.5 for wet soil
α, n = independent parameters
m = 1-1/ n
Fixed

## Slide 58
Bouwer, H., Groundwater Hydrology, McGraw-Hill, 1978
van Genuchten (1980), requires estimated “air entry value”, hs

## Slide 59: Solution schemes
Hydrus2D:
  Galerkin type linear finite element
  Time integration through implicit (backwards) finite difference scheme
  Solution through Gaussian elimination, conjugate gradient, or ORTHOMIN methods
  Adaptive time stepping

## Slide 60: Model configuration
2D vertical slice - finite element mesh
Atmospheric boundary
Seepage face boundary
Observation nodes

## Slide 61
October 2005 – draining from saturation – minimal evaporation
Upper piezometer
Outflow hydrograph

## Slide 62
October 2005 – draining from saturation – minimal evaporation
Predicted pressure head
Upper piezometer
Modeled outflow
Error = 19 cm

## Slide 63
October 2005 – draining from saturation – minimal evaporation
Upper piezometer
Modeled outflow
Error

## Slide 64
October 2005 – draining from saturation – minimal evaporation
Measured pressure head
Upper piezometer
Measured outflow

## Slide 65
October 2005 – draining from saturation – minimal evaporation
Modeled outflow
Modeled Pressure head

## Slide 66
Soil moisture characteristic curves are extremely sensitive to the calibration criterion used:

## Slide 67
.1
Pressure head vs water content
K vs pressure head

## Slide 68
.1

## Slide 69
.1

## Slide 70
.1

## Slide 71
.1
Ks = 132 cm/hr
Ks = 1 cm/hr

## Slide 72
Piezometer 1 calibration
p1
Saturated area
Flow calibration
flow
Time = 0 hour
Ks= 132 cm/hr
Ks=1 cm/hr
Hydrus2D
Drain from saturation
Inverse simulations

## Slide 73
Time = 1 hour
Piezometer 1 calibration
Flow calibration
p1
flow
Ks= 132 cm/hr
Ks=1 cm/hr

## Slide 74
Time = 10 hours
Piezometer 1 calibration
Flow calibration
p1
flow
Ks= 132 cm/hr
Ks=1 cm/hr

## Slide 75
Time = 20 hours
Piezometer 1 calibration
Flow calibration
Large saturated area
Small saturated area
p1
flow
Ks= 132 cm/hr
Ks=1 cm/hr

## Slide 76
p1
flow
Ks= 132 cm/hr
Ks=1 cm/hr
Huge difference in saturated and unsaturated domains
Vastly different response to rain and generation of pressure fields

## Slide 77
Assignment question:
12. What is the Dupuit-Forchheimer (DF) equation?
What is the requirement for Dupuit flow?

## Slide 78
Time = 1 hour
Piezometer 1 calibration
Flow calibration
p1
flow
Ks= 132 cm/hr
Ks=1 cm/hr
Is this a streamline?
Do the saturated profiles satisfy Dupuit theory?

## Slide 79
How good is this calibrated model in prediction mode?
Case 1. Initial moisture state completely known; evaporation losses are minimal
Case 2. Initial moisture state not known; evaporation losses are minimal
(Rain data are from surface rain gauge)

## Slide 80
Case 1: Hydrus2D simulation: 12-days starting from saturation, October, 2005 –
Measured flow

## Slide 81
Case 1: Hydrus2D simulation: 12-days starting from saturation, October, 2005 –
Calibration
Prediction
critical importance of knowing initial conditions

## Slide 82
Case 2: Hydrus2D simulation: 10 days starts November, 2004 –
initial conditions unknown -- assumed moderately dry
Simulated-best calibration from October 2005 test

## Slide 83
Case 2: Hydrus2D simulation: 10 days starts November, 2004 –
initial conditions unknown -- assumed moderately dry
Results from incorrect initial spatial soil water pattern

## Slide 84
Model predictions for biased and erroneous input time series
Bias in rain
Bias in potential evapotranspiration
Identical initial conditions for all scenarios

## Slide 85: Atmospheric measurements
Precipitation - TB3 gauges
Wind affected - uncorrectable
Under catch in gusty storms

## Slide 86: Atmospheric measurements
Precipitation – TB3 gauges
Wind speed
Air temperature
Relative humidity

## Slide 87: Radiation measurements
Solar (shortwave)
Atmospheric (longwave)
Surface temperature
Net radiation

## Slide 88: Soil heat flux measurements
Soil heat flux
Soil temperature
Figure source: Campbell Scientific HFT3 manual

## Slide 89: Internal state measurements
Water contents
Water content reflectometers
Time domain reflectometers (TDR’s)

## Slide 90
Output: Evapotranspiration (ET)
Turc (1961)
Hargreaves et al (1985)
3. Priestley and Taylor (1972)
4. Penman Monteith
5 calculation methods
5. Energy budget residual
Increasing measurement requirements
Indirect
Partially empirical
Highly uncertain

## Slide 91
Output: Evapotranspiration (ET)
Turc (1961)
Hargreaves et al (1985)
3. Priestley and Taylor (1972)
4. Penman Monteith
5 calculation methods
5. Energy budget residual
Available August 2004 -
Available September 1994 -

## Slide 92
ET April 22-23, 2005
ET (mm/hr)
Day
Empirical
Energy-based
Low
High

## Slide 93
BG1 and BG2 are “Weather Measure” 193 mm accumulators.
Gauges do not differ by more than 0.02 inches in any storm

## Slide 94
RBG1 – Hydrologic Services TB3 200 mm 0.2 mm/tip tipping bucket gauge.
Plots 1 and 2 (P1 and P2).

## Slide 95
BG2 is the reference rain gauge.

## Slide 96
Prof Jim Dooge
(1922 - 2010)
wise counsel and friend
Supervising SJB
RG2 reference
gauge - April 2001
International Hydrology Prize: Dooge Medal
Named to honor Jim in 2014

## Slide 97
Tipping bucket gauge (calibrated) annually.
Installed August 1994.
Not recommended.
Gauges installed as “checks” in later years.

## Slide 98
2003 measured cumulative fluxes
Benchmark rain
January 1
May 31
Rain undercatch
Bias

## Slide 99
2003 measured cumulative fluxes
Benchmark rain
Most rain becomes subsurface flow
More water lost to ET
January 1
May 31

## Slide 100
2003 measured and modeled cumulative fluxes
Benchmark rain
Turc
Turc x 2
ET: S-Wave radiation, Temperature, R-H; Turc, 1961

## Slide 101
2003 measured and modeled cumulative fluxes
Benchmark rain
HYDRUS modeled flow
19%

## Slide 102
2003 measured and modeled cumulative fluxes
Benchmark rain
Modeled flow
Bias

## Slide 103
Use of biased wind affected rain catch and low potential ET yielded approximately the correct cumulative hydrograph.
Modern methods of model parameter estimation would have used these typically available erroneous signals to determine hillslope hydraulic properties.

## Slide 104
Any such calibrated model would yield approximately the “right answer” concerning streamflow representation but have completely wrong soil water properties.
Such a model would be unsuitable (and indefensible) for prediction of changed “land-use” or for changed inputs, e.g. climate change.

## Slide 105
The TB3 pit gauge’s under-catch results from funnel airflow restrictions in the siphon delivery system in gusty storms.
This is documented in Kampf and Burges, J of Hydrology, 2010.

## Slide 107
How good is the newest climate network?

## Slide 108
BAMS April 2013

## Slide 110
What essential measuring device is missing?

## Slide 111
Do you see a pit rain gauge in this network?

## Slide 112
Topics:
Model Definitions and Modeling the water budget
Calibrating and testing a conceptual model using error free data
Calibration and test of a sophisticated soil physics based model and demonstration of the importance of accurate, bias-free measurements
Modeling a small watershed

## Slide 113: Tarrawarra, Australia
0.5 x 0.2 km catchment
Three-dimensional
Converging and diverging topography
Surface and subsurface flow

## Slide 114: Tarrawarra measurements Western and Grayson, 1998
74 piezometers
20 neutron probes (water content profiles)
10 m Digital Elevation Model

## Slide 115: Soil moisture (water content) measurements
13 moisture distributions
500 measurements each
Roving TDR measurements from the ‘green machine’
Images: http://www.civag.unimelb.edu.au/~western/tarrawarra/tarrawarra.html
Plan view moisture

## Slide 116: Framework of knowns/unknowns:
Domain: Size and boundary conditions
Characteristics: surface and subsurface
Input: Precipitation
Output: surface and subsurface
Internal states and fluxes: surface and subsurface
Clues…
but mostly unknown
Need fewer
uncertainties
for effective
model testing

## Slide 117
Tarrawarra simulations Keith Loague and Ben Mirus, Stanford University
3D fully coupled surface-subsurface flow
Integrated hydrology model (InHM) VanderKwaak (1999)
Figure: B. Mirus
Represents all physical mechanisms of water movement
Finite element numerical solution scheme

## Slide 118
Yet we lack:
comprehensive data sets for testing simpler models
methods of measuring at large scales
Practical distributed modeling applications require:
simpler, less computationally intensive models
coarser spatial resolution

## Slide 119
Tarrawarra-based hypothetical reality Keith Loague and Ben Mirus, Stanford University – Mirus et al, 2009
3D fully coupled surface-subsurface flow
Integrated hydrology model (InHM) VanderKwaak (1999)
Figure: B. Mirus
Represents all physical mechanisms of water movement
Finite element numerical solution scheme
Generate 10-year continuous simulations with known:
Domain
Characteristics
Input
Ouput
Internal states and fluxes

## Slide 120
Hypothetical reality test bed of ‘error-free’ measurements
Point time series
Stream flow
Water contents
Saturated water levels
Pressure heads
Spatial distributions
Water contents
Saturated water levels
Pressure heads
3D head distribution
Streamflow
time series

## Slide 121
Spatial pattern comparisons
Measurements
Model
Point locations
Convert to 20 m grid cells
Spatial interpolation: Kriging
InHM mesh
Contoured values
InHM mesh and model data courtesy of B. Mirus
Average cell value

## Slide 122
Model | Surface | Subsurface | Solution | Coupling
MODHMS (Panday and Huyakorn, 2004) | 2D diffusion | 3D Richards | Finite difference | First order or linked
Recently completed work – Dr. Nicoleta Cristea
Exploring model features of MODHMS
Model structure features:
variable spatial resolutions – plan view and vertical
surface-subsurface coupling schemes
E-T schemes
Cristea and Burges, 2024

## Slide 123
Topics:
Model Definitions and Modeling the water budget
Calibrating and testing a conceptual model using error free data
Calibration and test of a sophisticated soil physics based model and demonstration of the importance of accurate, bias-free measurements
Modeling a small watershed
Suggestions for a way forward

## Slide 124
My objective was to demonstrate the need for more complete measurements than are typically available and used in hydrologic model development and calibration.
I doubt we will make much more progress by solving multi-objective stochastic optimization formulations to determine model parameters using data of dubious quality.

## Slide 125
Unknown time-varying biases and stochastic errors in precipitation and potential ET cannot be represented by any plausible Bayesian prior distributions.
There is no substitute for accurate model input time series.

## Slide 126
We can make substantial progress by putting in place hydrologically useful rain measuring networks. (e.g., Sieck, Burges and Steiner, WRR, 2007.
We must make substantially improved measurements from which we can determine unbiased evaporative fluxes.

## Slide 127
Models need to be constructed using unbiased inputs that also include measurements of hillslope states.
Such models will have credibility when used to predict the hydrologic consequences of land-use change or climatic change.
Existing approaches using crude data are not up to the task.

## Slide 128
Few (if any) of the subsurface geometric details are measured – they are critical
Almost no states are measured
Few flow-path fluxes are measured
Should they be measured and modeled?
Yes!

## Slide 129
We need to determine what to measure and how to model in complex topography to
gain insight into floods and
determine landslide and debris flow risk.

## Slide 130
Hydrologists, however, need to stay close to their “laboratories”.

## Slide 132
References:
Crawford, N. H. and Burges, S. J., (2004), History of the Stanford Watershed Model, Water Resources Impact, 6(2), 3-5.
Cristea, N. and Burges S., Hydrologic effects of evapotranspiration representation in a 3-D coupled surface-subsurface distributed hydrologic model at the catchment scale, in review (Hydrologic Processes, June 2024)
Feyen, Luc, Jasper A. Vrugt, Breanndan O Nuallain, Johan van der Knijff, Ad De Roo, (2007) Parameter optimisation and uncertainty assessment for large-scale streamflow simulation with the LISFLOOD model, Journal of Hydrology 332, 276–289.
Gan T. Y., and Burges, S. J., (1990 ) An assessment of a conceptual rainfall-runoff model's ability to represent the dynamics of small hypothetical catchments, 1: models, model properties, and experimental design, Water Resources Research, 26(7), 1595-1604.

## Slide 133
James, L.D. and S.J. Burges (1982) Selection, Calibration, and Testing of Hydrologic Models, Chapter 11 in C.T. Haan, H.P. Johnson and D.L. Brakensiek, eds, Hydrologic Modeling of Small Watersheds, American Society of Agricultural Engineers, Hydrologic Modeling Monograph.
Kampf, Stephanie K., (2006) Towards Improved Representation of Hydrologic Processes: Linking Integrated and Distributed Hydrologic Measurements to a Physically-Based Model for a Planar Hillslope Plot, Water Resources Series Technical Report No. 183, Dept. of Civil and Environmental Engineering, University of Washington, 214p.
Kampf, S. K., and S. J. Burges (2007), A framework for classifying and comparing distributed hillslope and catchment hydrologic models, Water Resour. Res., 43, W05423, doi:10.1029/2006WR005370.
Kampf, S. K., and S. J. Burges (2007), Parameter estimation for a physics-based distributed hydrologic model using measured outflow fluxes and internal moisture states, Water Resour. Res., 43, W12414, doi: 10.1029/2006WR005605.
Kampf, S. K., and S. J. Burges (2010), Quantifying the water balance in a planar hillslope plot: effects of measurement errors on flow prediction, Journal of Hydrology, 380 191-202, doi:10.1016/j.jhydrol.2009.10.036.

## Slide 134
Gan T. Y., and Burges, S. J., (1990 ) An assessment of a conceptual rainfall-runoff model's ability to represent the dynamics of small hypothetical catchments, 2: hydrologic responses for normal and extreme rainfall, Water Resources Research, 26(7), 1605-1619.
Kolsti, K.F., S.J. Burges, and B.W. Jensen (1995) Hydrologic Response of Residential-Scale Lawns on Till Containing Various Amounts of Compost, Water Resources Series, Technical Report #147, Department of Civil Engineering, University of Washington, p143.
Loague, K., J.E. VanderKwaak. (2004) Physics-based hydrologic response simulation: platinum bridge, 1958 Edsel, or useful tool, Hydrological Processes, 18:5737.
Mirus, B. B., K. Loague, J. E. VanderKwaak, S. K. Kampf, and S. J. Burges (2009), A hypothetical reality of a Tarrawarra-like hydrological response, Hydrological Processes, 23(7), 1093-1103, doi:10.1002/hyp.7241.
Panday, S., Peter S. Huyakorn. (2004) A fully coupled physically-based spatially-distributed model for evaluating surface/subsurface flow, Advances in Water Resources, 27:361-382.

## Slide 135
Sieck, L.C., S. J. Burges, and M. Steiner (2007), Challenges in obtaining reliable measurements of point rainfall Water Resources Research, 3(1),W0142010.1029/2005 WR004519.
Šimùnek, J., M. Sejna, M. Th. van Genuchten, (1999 ) The HYDRUS-2D software package for simulating two-dimensional movement of water, heat, and multiple solutes in variably saturated media, in International Ground Water Modeling Center, Colorado School of Mines, Golden, Colorado.
Šimùnek, J., Nick J. Jarvis, M. Th. van Genuchten, Annemieke Gardenas, (2003) Review and comparison of models for describing non-equilibrium and preferential flow and transport in the vadose zone. Journal of Hydrology 272:14-35.
VanderKwaak, J. E., (1999) Numerical simulation of flow and chemical transport in integrated surface-subsurface hydrologic systems. University of Waterloo, Waterloo, Ontario, Canada.
Western, A. W., R.B. Grayson, (1998) The Tarrawarra data set: Soil moisture patterns, soil characteristics, and hydrological flux measurements. Water Resources Research 34:2765-2768.

## Slide 137
Bouwer, H., Groundwater Hydrology, McGraw-Hill, 1978

## Slide 138
Bouwer, H., Groundwater Hydrology, McGraw-Hill, 1978

## Slide 139
Bouwer, H., Groundwater Hydrology, McGraw-Hill, 1978

## Slide 140
Hillel, D., Environmental Soil Physics, Academic Press, 1998 – Chap 14