## Slide 1
Near headwaters of Healy Creek, Banff National Park 9/11/2014

## Slide 2
Some Lessons Learned Working in Hydrology and Water Resources Engineering for Fifty-seven Years
Stephen J. (Steve) Burges
Professor Emeritus
Department of Civil and Environmental Engineering
University of Washington, Seattle, WA
CEE 500 Seminar
230 More Hall, University of Washington
April 11, 2024

## Slide 3
A personal assessment of time and place:
World events that influenced deployment of capital, attention to societal concerns about flooding, droughts, and pollution abatement and cleanup, have influenced what research could be done and when.
Advice from mentors, and the interests of my collaborating colleagues, have influenced the research topics addressed.

## Slide 4
The developments in instruments, space‐based remote sensing of planet Earth, and computing and information transfer have defined the timing of much of our work.
One of the largest challenges all of us face is deciding what evolving technologies to embrace.

## Slide 5
Whenever possible, I tried to work on topics for which I thought we would need improved tools (including observations) about 10–20 years before they were needed.

## Slide 6
Topics

## Slide 7
Landmark technological developments 1944 -
Follow up technology
Issues in hydrology and water resources engineering
The importance of mentors
Choosing research topics
Take home message

## Slide 8
Landmark technological developments 1944 -

## Slide 9
Point Contact Transistor
Bell Labs
First demonstration December 23, 1947
Replaced vacuum tube “triode”.

## Slide 10
John Bardeen – one of only 5 scientists to win two Noble Prizes
(Superconductivity)
Marie Curie
Linus Pauling
Frederic Sanger
Barry Sharpless
1956 Nobel Prize in Physics

## Slide 11
James Watson and Francis Crick
Nature 1953
“Double helix”
1962 Nobel Prize
in Physiology or Medicine

## Slide 13
1 Page !

## Slide 14
Television – Australia - 1956
Vacuum tube technology
Precursor of modern screens

## Slide 15
Sputnik - 1 USSR - October 4, 1957
83.6 Kg
Orbital Period 96.2 minutes

## Slide 16
Integrated Circuit (IC):
Jack Kilby’s original IC 1958
Kilby awarded the Nobel Prize in Physics (2000)
~ 0.5 inch
Human-hair-size (70,000 nm) “bonding wires” used to wire together separate transistors, capacitors, and resistors into a circuit.
Now called “hybrid” integrated circuits.

## Slide 17
Future Nobel Laureate, Richard P. Feynman, 1959
“There's Plenty of Room at the Bottom”

## Slide 18
Miniaturizing the computer
Why can't we make them very small, make them of little wires, little elements - and by little, I mean little.
For instance, the wires should be 10 or 100 atoms in diameter, and the circuits should be a few thousand angstroms across.

## Slide 19
LASER - Light Amplification by Stimulated Emission of Radiation
Theodore Maiman
built first functional laser
- May 16, 1960

## Slide 20
Stimulated Optical Radiation in Ruby, T. H. Maiman, Nature 187, 493–494, 1960

## Slide 22
< 3/4 Page !

## Slide 23
Stimulated Optical Radiation in Ruby, T. H. Maiman, Nature 187, 493–494, 1960
"probably more important per word than any of the papers published by Nature over the past century.“
Obituary - Theodore H. Maiman (1927–2007), Charles Townes, Nature, 2007.
Dr Townes shared the 1964 Nobel Prize in Physics for inventing the LASER and MASER

## Slide 24
Neil Armstrong, Michael Collins, Edwin E. Aldrin, Jr.
First Humans on the Moon - Apollo 11 July 20, 1969
Edwin E. Aldrin, Jr. and Lunar Module “Eagle”
Space exploration program – major influence on speed of technological development

## Slide 25
Landmark technological developments 1944 -
Follow up technology

## Slide 26
Hewlett-Packard
HP 35 pocket calculator
35 function keys
1972 – 1975
100,000 sold in the first year
@ more than $300 = $2,270 today

## Slide 27
HP 35 circuit board
Mostek 6020 Integrated Circuit

## Slide 28
Modern Theodolite
Total Station – huge advance
Electronic distance measuring
laser and prism
Angular measurements
Automatic data reduction
x, y, z
Combined: LASER, Theodolite, and “calculator”

## Slide 29
Fiber optic data transmission – since about 1981

## Slide 30
GRACE up to June 2017

## Slide 31
The importance of LANDSAT:
52nd - year - continuous mapping of earth’s surface
LANDSAT 1 launched July 23, 1972
LANDSAT 9 launched September 27, 2021

## Slide 32
From: MIT Technology Review
Cover Story, By Alice Dragoon, June 29, 2021
“The woman who brought us the world”
“A half-century ago, Virginia Tower Norwood ’47 invented the first multispectral scanner (MSS) to image Earth from space. Landsat 1 and its successors have been scanning the planet continuously ever since”.
https://www.technologyreview.com/2021/06/29/1025732/the-woman-who-brought-us-the-world/

## Slide 33
Every user of LANDSAT data owes a huge debt to Virginia T. Norwood (1/8/1927 – 3/26/2023) for her exceptional vision, scientific, engineering, and managerial skills. Elected a member of NAE February, 2023.
Virginia Norwood - Photo by Michelle Groskopf
See also - Virginia T. Norwood: The Mother of Landsat
https://landsat.gsfc.nasa.gov/article/virginia-t-norwood-mother-landsat

## Slide 34
NASA Earth Fleet – December 2023
SWOT Surface water and ocean topography, Dec 15, 2022
GRACE - FO (2), May 22, 2018
Ice, cloud and land elevation satellite-2, Sep. 15, 2018
SMAP Soil Moisture – Active - Passive observatory, 2015

## Slide 35
Advances during my lifetime in:
computers
All forms of “surveying” the states of the earth’s “critical zone”
Information transfer
Data storage and retrieval
Accessibility of the “libraries” of the world
Were unimaginable fifty-seven years ago

## Slide 36
Example: Some advances in computing tools

## Slide 37
My first FORTRAN code - 1966
IBM 1130 Computer

## Slide 39
IBM 1130 Computing System 1965
64 K bytes of core memory!

## Slide 40
1967
IBM 1316 removable disk pack
4 inches deep; six 14 inch disks, 10 lb;
Capacity 7.25 M bytes
2021
2 T Bytes $40

## Slide 41
https://www.bing.com/images/search?view=detailV2&ccid=GgOYvCQU&id=9B52DDF1E482EAF6A551495E0E38D0D2816AE1C1&thid=OIP.GgOYvCQUb78s_8asNXt1mwHaFP&mediaurl=http%3A%2F%2F1.bp.blogspot.com%2F-qbgpKYJu3x8%2FUToyTVxkicI%2FAAAAAAAAAE8%2FQP3dotSINo0%2Fs1600%2FMobile-Phones.jpg&exph=1131&expw=1600&q=smartphone+images&simid=608012722465147338&selectedindex=39&qpvt=smartphone+images&ajaxhist=0
Hand – held “super computers”
Approaching Feynman’s “little”
Transistor Industry Standard 7 nm, 2021
3 nm, in production - 2024
IBM has developed a 2 nm transistor

## Slide 42
There have been many who did not see a bright future following World War II, the Korean and Vietnam Wars.
Their concerns were for nuclear war, challenges of population growth, and possible famines.
Fortunately, all proved wrong.

## Slide 43
End-of-the-world novel
World War III – Nuclear holocaust
Melbourne Australia –
last survivors 1964
Cold war – possibility of nuclear annihilation
Nevil Shute (Norway) 1957

## Slide 44
Doom and gloom about world population, 1968
1970 - 3.7 billion
2024 - 8.0 billion - U.N. Est.

## Slide 45
Famine and extreme pessimism
Triage, whole countries
“written off”, 1967
Completely missed the “green revolution”

## Slide 46
Despite great geopolitical turbulence, doom and gloom about the future, and world-wide inhumanity during my life (1944 -), with all these advances, I remain an optimist for on-going progress in all we do.
Burges, wrr, 2011

## Slide 47
wrr, 2011

## Slide 48
wrr, 2011
I conclude with a long‐term community “grand challenge,” the coupled modeling of the ocean‐atmosphere‐landform hydrologic cycle for the purpose of long–lead time hydrologic prediction.

## Slide 49
Landmark technological developments 1944 -
Follow up technology
Issues in hydrology and water resources engineering

## Slide 50
1. Earth energy balance and the “hydrologic cycle”

## Slide 51
Thermal energy balance of planet earth
Fig 7. The global annual mean energy balance of Earth for approx. 2000 – 2010.
All fluxes are in Watts/m2 Image credit: Graeme Stephens
340.2 +- 0.1
239.7 +- 3.3
100.0 +- 2

## Slide 52
Thermal energy balance of planet earth
Fig 7. The global annual mean energy balance of Earth for approx. 2000 – 2010.
All fluxes are in Watts/m2 Image credit: Graeme Stephens
Principal elements of atmospheric energy balance
75 +- 10
24 +- 7
88 +- 10
-187.9 +- 12.5

## Slide 53
Thermal energy balance of planet earth
Fig 7. The global annual mean energy balance of Earth for approx. 2000 – 2010.
All fluxes are in Watts/m2 Image credit: Graeme Stephens
Principal elements of atmospheric energy balance
75 +- 10
24 +- 7
88 +- 10
-187.9 +- 12.5
0.6 +- 0.4

## Slide 54
Thermal energy balance of planet earth
Fig 7. The global annual mean energy balance of Earth for approx. 2000 – 2010.
All fluxes are in Watts/m2 Image credit: Graeme Stephens
Principal elements of atmospheric energy balance
75 +- 10
24 +- 7
88 +- 10
Uncertainties
-187.9 +- 12.5
0.6 +- 0.4

## Slide 55
2. Global Importance of Soil

## Slide 56
Source – Orgiazzi, A., et.al. (Eds.), 2016, Global Soil Biodiversity Atlas. European Commission, Publications Office of the European Union, Luxembourg. 176 pp.
Major hydrologic change

## Slide 57
Source – Orgiazzi, A., et.al. (Eds.), 2016, Global Soil Biodiversity Atlas. European Commission, Publications Office of the European Union, Luxembourg. 176 pp.

## Slide 58
Source – Orgiazzi, A., et.al. (Eds.), 2016, Global Soil Biodiversity Atlas. European Commission, Publications Office of the European Union, Luxembourg. 176 pp.
America’s

## Slide 59
Source – Orgiazzi, A., et.al. (Eds.), 2016, Global Soil Biodiversity Atlas. European Commission, Publications Office of the European Union, Luxembourg. 176 pp.
Rest of World

## Slide 60
3. First quantitative measures of atmospheric global precipitable moisture

## Slide 61
Source: GEWEX News-August 1994
Jan
Dec

## Slide 62
Source: GEWEX News-August 1994

## Slide 63
Average precipitable moisture in the atmosphere:
Approximately 24 mm (almost 1 inch).
Approximately 1.64 x 1013 Tonnes

## Slide 64
4. Fundamental Hydrology
Hydrology is concerned with determining the water budget and associated thermal energy budget (evaporation, snow and ice)

## Slide 65
A major effort is in rainfall-runoff modeling
Choose model
Define the catchment boundaries
– subsurface not well defined
Select input time series
– precipitation, potential evapotranspiration
Determine suitable model parameters
– usually by forcing the predicted streamflow
time series to match the observed time series

## Slide 66
When records are relatively good, where will we experience the greatest modeling difficulties?

## Slide 67
Consider the conterminous US
Approximately two thirds of the precipitation is evaporated or transpired.

## Slide 68
Conterminous (CONUS) U.S.
Maps of average annual,
Precipitation,
Runoff

## Slide 69
PRISM model 1961 - 1990

## Slide 70
http://www.bing.com/images/search?q=map+of+US+annual+runoff
Average US Annual Runoff

## Slide 71
Caution – Users of “big data”
What challenges are faced when constructing an “average annual runoff map”, or any spatial data map?
Know the limitations of the data set!
First heroic effort for CONUS – USGS 1949 – using measured streamflow and hand drawn contours.
USGS professional staff had extensive knowledge of all data records used.

## Slide 73
Major variation in contours – exceptional detail
First mapping – annual average runoff, CONUS -1949

## Slide 74
Langbein et al, 1949 – Summary page 12
“Annual runoff from the United States
ranges from less than a quarter of an inch in
the intermountain deserts to more than 80
inches in the Olympic and Cascade Mountains of
Washington and Oregon.
The country-wide average is approximately 8.5 inches, which, subtracted from the average precipitation of 30 inches, indicates that evapotranspiration loss is about 21.5 inches”.

## Slide 75
What climatic regions pose the greatest difficulties for, and create the greatest need for, improved precipitation measurement?

## Slide 76
Mixed snow & rain
Convective storms
Infrequent storms
Atmospheric River storms

## Slide 77
What regions have the least runoff signal for model building, calibration, and testing?

## Slide 78
http://www.bing.com/images/search?q=map+of+US+annual+runoff
Average US Annual Runoff
Minimal signal

## Slide 79
http://www.bing.com/images/search?q=map+of+US+annual+runoff
Average US Annual Runoff
Barely adequate, extremely challenging

## Slide 80
5. Hydrology and water resources
The principal societal and ecological issues in hydrology and hydrologic and water resources engineering are (in no particular order):

## Slide 81
Water storages - Liquid
“Interception”

## Slide 82
“Depression storage”

## Slide 83
“Soil Moisture”

## Slide 84
“Soil Moisture”

## Slide 86
Principal aquifers - CONUS
Surface - sub surface flow paths – aquifer storage

## Slide 87
Surface water storages - solid

## Slide 89
Floods
The river owns the valley

## Slide 90
Hurricane Katrina New Orleans- blogs.sacbee.com
http://www.bing.com/images/search?q=Hurricane+Katrina&Form=IQFRDR#view=detail&id=95874B1E3A338360117159C7FE90C2530DECD7E1&selectedIndex=31
New Orleans – aftermath of Hurricane Katrina - Aug 23, 2005 – Aug 31, 2005

## Slide 91
Ice - jam flooding

## Slide 92
http://i.dailymail.co.uk/i/pix/2013/05/30/article-2333098-1A0DBEC2000005DC-337_968x665.jpg
Alaska, 2013

## Slide 93
http://media.cleveland.com/plain-dealer/photo/2014/01/14081485-standard.jpg
Ohio, 2014

## Slide 94
http://www.weather.gov/images/cle/Wx_Events/2014/IcejamFeb212014/P1000602.JPG
Ohio, 2014

## Slide 95
Green Circles—
Al Khufrah Oasis, Libya, October 28, 2004
Water for food and fiber

## Slide 97
http://www.es.lancs.ac.uk/people/johnq/New%20Folder/steppingley%20gully.jpg
Water as a “change agent”

## Slide 98
http://www.uwsp.edu/geo/faculty/ritter/images/lithosphere/mass_wasting_erosion/sheet_erosion_large.jpg
“Transport agent” – sediments – dissolved substances

## Slide 99
Lake Lanier, Georgia - Brian Hursey
March 4th 2007
February 11th 2008
Virginia riverbed - NASA
Drought

## Slide 101
Severe Drought 1984-1985 – NASA NVDI
Dark color –
Most severe

## Slide 102
Ground water use including for drought mitigation
Ground water reservoirs have known supply:
considerable uncertainty about supply from surface reservoirs leading up to, and during drought
Time history of US ground water use: 1900 - 2000 -2008

## Slide 103
113
145
118
182
259
341
145 cubic km = 117.6 MAF = 7.8 yr. crf.
Mean ann. flow Colorado R. = 15 MAF
Leonard F. Konikow, Groundwater Depletion in the United States (1900−2008), USGS Scientific Investigations Report 2013−5079

## Slide 104
Water supply
surface storage
transport

## Slide 105
Potable water

## Slide 106
Water for ecology

## Slide 107
Salmon deaths – insufficient water

## Slide 108
Urban Land use
Google Earth, Seattle
1 mile

## Slide 109
Google Earth, Seattle
Urban Land use

## Slide 110
Urban land use – heterogeneity - Land surface – atmosphere interactions
Landsat image

## Slide 111
Landsat
Puget Sound
35 km
Lake Washington

## Slide 112
Landsat
Vegetated domain
Urban domain
Different mixes of latent (evaporative) and sensible heat
Added anthropogenic
sensible heat

## Slide 113
Urban hydrology:
hydrologic and hydro-ecological infrastructure design, operation, and maintenance

## Slide 114
Large expenditures are needed for hydrologic engineering infrastructure design and redesign for ecological and societal resilience and water reuse.

## Slide 115
Hydrologic change when converting land for farming and forest harvesting

## Slide 117
Permanent change in temporal and spatial water budget, albedo, and latent and sensible heat
Increased wind and water erosion potential

## Slide 118
Decadal-scale change in temporal and spatial water budget, albedo, and latent and sensible heat
Increased water erosion potential

## Slide 119
Landscape change - fire and renewal
Transient decadal-scale change in temporal and spatial water budget, albedo, and latent and sensible heat

## Slide 120
Landscape change - ecological imbalance
Trees killed by pine bark beetles

## Slide 121
https://www.bing.com/images/search?view=detailV2&ccid=6uUrDSIF&id=E687146CB86981439D2770C1837E1E5B4D7B73BC&thid=OIP.6uUrDSIFNgD_07ocYbDiSQHaE6&mediaurl=http%3a%2f%2fwww.ellingsoncompanies.com%2fwp-content%2fuploads%2f2014%2f04%2fIMG_1450.jpg&exph=1360&expw=2048&q=agricultural+land+drainage&simid=608047902956847224&selectedIndex=103&ajaxhist=0
Agricultural land drainage
Surface - “ditch” - drainage

## Slide 122
https://www.bing.com/images/search?view=detailV2&ccid=F8QjwaBR&id=D8CA61F29E20F5FDAC91879F031CCE8AC1F5D33F&thid=OIP.F8QjwaBR39kdI8Ck90aXPgHaDS&mediaurl=https%3A%2F%2Fwww.cotterillcivils.co.uk%2Fwp-content%2Fuploads%2F2017%2F03%2Fland-drainage-1000x445.jpg&exph=445&expw=1000&q=agricultural+land+drainage&simid=608033089580305690&selectedindex=435&ajaxhist=0
Subsurface drainage

## Slide 123
https://www.bing.com/images/search?view=detailV2&ccid=mA8Dx4ae&id=C1F07B49F4ED46397DEA4227954792CF2B650B45&thid=OIP.mA8Dx4aeIBMPi96cJVlRogHaEK&mediaurl=http%3A%2F%2Ffootage.framepool.com%2Fshotimg%2Fqf%2F924111828-plantation-de-the-theier-culture-du-the-kenya.jpg&exph=540&expw=960&q=agricultural+land+drainage&simid=608005494415034365&selectedindex=372&ajaxhist=0
Permanent change in temporal and spatial water budget, subsurface hydrology, and latent and sensible heat
Enhanced transport of agrichemicals to rivers

## Slide 124
Page 481 - The Yearbook of Agriculture 1955 – Water, USDA, p751
5.4% CONUS

## Slide 125
2012 Census of Agriculture, United States-Summary and State Data-Vol. 1 - Geographic Area Series - Part 51 AC-12-A-51, May 2014 – Table 50 -Land Use Practices by Size of Farm - 2012
2012
Subsurface drainage 48.6 million Acres
Surface drainage 42.2 million Acres
Total 90.7 million Acres
4.8% CONUS

## Slide 126
Some consequences of farming practice and resulting hydrologic fluxes

## Slide 129
Extensive work has been done on how “legacy nitrogen” limits water quality improvement in The Gulf of Mexico by Professor Nandita Basu, University of Waterloo

## Slide 130
Van Meter et al., Science 360, 427–430 (2018)
Science - 2018

## Slide 131
Virtual water transfers
Major work by Professor Megan Konar, University of Illinois, Urbana-Champaign

## Slide 132
Virtual water flows - state to state:
317 billion m^3/yr
257 MAF
17 years Colorado R. flow
Source
Fraction
Agricultural virtual water flows within the United States, Dang, Lin, Konar, wrr 2015
TX
CA

## Slide 133
6. Scientific hydrology and hydrologic engineering
Developments in hydrologic science have been driven, and will likely continue to be driven, by societal needs.
It is essential that the best practicable science be used in professional practice.
Some guiding principles for advancing hydrologic science:

## Slide 134
Eagleson Committee 1991
Unifying, holistic view of hydrologic sciences

## Slide 135
An integrative framework for much of hydrologic science has been provided by focusing on the “Critical Zone”, first introduced in:
“Basic Research Opportunities in Earth Science”, National Research Council, p 154, 2001

## Slide 137
I am guilty, together with Professor Gail Ashley (Rutgers) and the late Professor Larry Wilding (Texas A & M), for introducing this framework to the NRC Committee.
There are 46 Critical Zone Observatories globally.

## Slide 138
Figure 2. The current network of nine critical zone observatories funded in the United States to investigate all aspects of the critical zone. S. L. Brantley et al.: Designing a network of critical zone observatories, Earth Surf. Dynam., 5, 841–860, 2017

## Slide 139
Critical Zone

## Slide 140
Relative scales
Earth = 1 m
Mt Everest = 0.7 mm
Mariana Trench = 0.9 mm
Critical zone
Little known about the 1 m domain
Our domain is -0.1 to 0.7 mm above sea level

## Slide 141
1991 report; 20 - years on and exploring new opportunities:
NRC, 2012
Provides broad examples of the “promising new opportunities to advance hydrologic sciences”

## Slide 142
Community leadership in advancing hydrologic science in the U.S.
Consortium of Universities for the Advancement of Hydrologic Science, Inc. CUAHSI

## Slide 143
Are there possibilities for advancing hydrologic science using “Machine Learning”?

## Slide 144
2021

## Slide 145
Landmark technological developments 1944 -
Follow up technology
Issues in hydrology and water resources engineering
The importance of mentors

## Slide 146
We all need mentors across the age spectrum.
Engineering mistakes are repeated about every 30 years.
There is a loss of “institutional” memory over about 30 years – e.g., Oroville Dam spillway failure February 27, 2017
See Forensic Report: https://damsafety.org/sites/default/files/files/Independent%20Forensic%20Team%20Report%20Final%2001-05-18.pdf

## Slide 147
Oroville Dam, CA, failed spillway, Feb 27, 2017
https://en.wikipedia.org/wiki/Oroville_Dam#/media/File:Oroville_Dam_spillway_damage_27_Feb_2017.jpg
Cost of replacement of spillway 2017-2018 and stabilization below emergency spillway – 2018, $1.2B (DWR Feb. 2021)

## Slide 148
Seek a wise older (30 + years) mentor, and then others younger and older than yourself.
Seek, with help of mentors, examples of inspiring work.

## Slide 149
My mentors have influenced me in many ways:
Undergraduate - The University of Newcastle, Australia
Dr. Peter Kleeman, B.E. thesis supervisor
Professor Harold R. (Rupert) Valentine (92 – September 29, 2010)

## Slide 150
Graduate studies - Stanford
Professor Robert L. (Bob) Street, NAE, MS advisor
Professor Ray K. Linsley, Jr., NAE, (73 – November 6, 1990) Ph.D. advisor

## Slide 151
University of Washington:
Professor Eugene P. (Gene) Richey (86 - July 3, 2003)
Professor Colin B. Brown (84 – November 12, 2013)
Professor Ronald E. (Ron) Nece ( 92 - March 28, 2018)

## Slide 152
External:
Many wonderfully generous colleagues of all ages.

## Slide 153
Landmark technological developments 1944 -
Follow up technology
Issues in hydrology and water resources engineering
The importance of mentors
Choosing research topics

## Slide 154
Short academic history:
Engineering educator 1970 to 2010
Professor emeritus 2010 -
Worked on a wide range of topics, and where possible, to match the interests of my younger colleagues
Published a maximum of 2 papers per topic
Fortunate to have exceptional co-workers
For a complete list see CV at:
https://www.ce.washington.edu/people/faculty/burgess

## Slide 155
Major mid-career influence:
Nobel Laureate Sir Peter Medawar’s book “Pluto’s Republic”, 1982 - first read January 1993
Extract from his essay on induction:
"I reckon that for all the use it has been to science about four-fifths of my time has been wasted, and I believe this to be the common lot of people who are not merely playing follow-my-leader in research".
If only about 20 % of Sir Peter’s research was productive, the rest of us would be doing well if 5% of ours was potentially valuable.

## Slide 157
Research is similar to the inventing process; major progress takes many years.
An invention, on average, is about the 35th iteration of the original idea.
e.g.

## Slide 158
Research is constrained by the intellectual environment of the times and tools available:
measurement technology e.g. LIDAR
computing capability - data storage and access
computing tools (e.g., finite differences, finite elements, finite volumes, Kalman Filter)
software advances – rapid change and obsolescence is the norm.

## Slide 159
How have I chosen research topics?
Serendipity
Application of known principles to provide needed solutions to problems within a time frame of 5 years or so.
Identify topics that I thought would need new tools and understanding to solve emerging major societal problems related to the water cycle – time frame 10 to 20 years or longer.

## Slide 160
Serendipity – responding to short-term needs of regulatory agency colleagues
I attended the International Symposium on Uncertainties in Hydrologic and Water Resources Systems, University of Arizona in December 1972
Invited lecture: C. Allin Cornell (MIT), First-Order Analysis of Model and Parameter Uncertainty
Allin showed how to propagate the mean and variance of independent variables in any model. I have used it extensively since then.

## Slide 161
First-order uncertainty propagation for the Streeter-Phelps equations.
Findings guided the building of EPA's QUAL2E Model

## Slide 162
Serendipity – subtle guidance by a precious mentor

## Slide 163
Arthur E. Morgan
Chief Engineer,
Miami Conservancy District
ASCE

## Slide 164
ASCE
Systems included:
Canals and Waterborne Transportation (Erie Canal)
Complex Water Supply System (New York City)
Flood Mitigation Planning (Miami Conservancy District)
Irrigated Agriculture in the West (Colorado River System – Hoover Dam)
Multiple Purpose Systems (Tennessee Valley Authority - TVA)

## Slide 165
Ray Linsley asked me in 1976 to write this paper. He suggested that I might find the works of “The Miami Conservancy District” informative.
Thus began my 47 years historical interest in this work and the work of Arthur E. Morgan.
I revisit it frequently for inspiration.

## Slide 166
504 pp
Excellent social-political-economic flood engineering
Rare 25-years post project effectiveness assessment

## Slide 167
The flood protection works of the Miami Conservancy District, have been in place since 1922.
Built following disastrous flooding in March 1913 in the Dayton, Ohio region - 360 bodies were recovered; hundreds disappeared.
An estimated 20,000 homes were destroyed in Ohio, mainly in the 4,000 square miles Great Miami River Valley.
Hamilton and Dayton suffered the greatest damage.

## Slide 168
Approximately 10 square miles of Dayton were inundated.
Excellent example of integrated flood damage disaster prevention and systems and life cycle engineering.

## Slide 169
Morgan and colleagues published Ten comprehensive “Technical Reports” between 1917 and 1922.
The reports describe some of the best scientific hydrology and hydrologic engineering work that has been done.

## Slide 170
What are the flood works of the Miami Conservancy District?

## Slide 171
Ohio River
Great Miami R.
Catastrophic Flood - March 1913

## Slide 172
https://www.mcdwater.org/wp-content/uploads/2017/04/Great-Miami-River-Watershed.png
District
15 Counties
Conservancy District – 1914
Entire catchment - 4,000 sq. miles, 15 counties
Model for governance and public infrastructure funding

## Slide 173
Pioneering work on reconstructing flood producing rain and assessing future possible major storms.
Exceptional scientific and engineering hydro-meteorological investigation and international data gathering and assessment.
Documented in Technical Reports Part V, 1917.

## Slide 174
50 miles

## Slide 175
5 major “dry” dams
Channel hydraulic improvements including 55 miles of levees
Gaps between levees are open flood plains

## Slide 176
Englewood Dam – largest of 5

## Slide 177
Englewood “Dry” Dam
Dry side
0.89 miles

## Slide 178
Ungated outlet works
Spillway
Fail-safe and safe-fail design.
No human intervention needed.

## Slide 179
First U.S. integrated river basin solution
First U.S. dams and levees engineering solution
Flooding and deaths – March 1913
Designs – 1915
Work completed – 1922

## Slide 180
There has not been a flooding problem since project completed in 1922.

## Slide 181
Example of exploring development of tools that may be needed in several decades.
Detection of climate signals in long-term records.

## Slide 182
Supported in part by National Science Foundation grant DEB74-20744-A02 to the Coniferous Forest Biome Ecosystem Analysis Studies.

## Slide 183
Example of benefit of operating a research site for a relatively long time:
Research site on UW eastern campus
Seven plots were constructed in 1994 (32 x 8 x 1 ft. deep) to determine if adding compost to till based soil could mitigate deleterious effects of typical suburban lawns.
I maintained these plots from 1998 to July 2009 largely to do extensive rainfall measurements and observe hydrologic processes.

## Slide 184
University of Washington
Experimental Plots Constructed 1994

## Slide 185
Plot 1
Weather Stations
Summer 2005

## Slide 186
Serendipity:
After several years, the plots were stable and grass well established. Four pit rain gauges installed permitted measuring rain accurately.
Stephanie Kampf recommended in 2004 that she and I instrument one plot so we could do an accurate water and thermal balance.
Resulting research:
Calibration and test of a sophisticated soil physics-based model and demonstration of the importance of accurate, bias-free measurements.

## Slide 187
Data from University of Washington site
Spatial hydrologic Model – Hydrus – 2D (Šimùnek, Sejna, van Genuchten, 1999)
Solves Richards’ equation for a variably saturated flow domain
Finite element solution scheme
Part of Professor Stephanie Kampf’s doctoral dissertation (2006); Kampf and Burges wrr, 2007, J of H 2010. (NASA and other graduate fellowships supported)

## Slide 188
Experimental plot
Till-based soil:
33% gravel;
45% sand;
17% silt;
5% clay
5 Piezometers

## Slide 189
Controlled Experiment - Draining from saturation:
Irrigate to saturation
Turn off water supply
Measure outflow hydrograph and soil moisture state
July 2005 and October 2005, (known initial conditions)

## Slide 190
Controlled Experiment - Draining from saturation:
Model calibration objective:
Determine soil hydraulic characteristic curves for assumed homogeneous soil

## Slide 191
Calibration: inverse simulations - Hydrus2D
Calibration and testing results are given in detail in Kampf and Burges, wrr 2007

## Slide 193
Illustration of model predictions for biased and erroneous input time series
Bias in rain
Bias in potential evapotranspiration
Identical initial conditions for all scenarios

## Slide 194: Atmospheric measurements
Precipitation - TB3 gauges
Wind affected - uncorrectable
Under catch in gusty storms
Cumulative volume check

## Slide 195: Atmospheric measurements
Precipitation – TB3 gauges
Wind speed
Air temperature
Relative humidity

## Slide 196: Radiation measurements
Solar (shortwave)
Atmospheric (longwave)
Surface temperature
Net radiation

## Slide 197: Soil heat flux measurements
Soil heat flux
Soil temperature
Figure source: Campbell Scientific HFT3 manual

## Slide 198: Internal state measurements
Water contents
Water content reflectometers
Time domain reflectometers (TDR’s)

## Slide 199
Output: Evapotranspiration (ET)
Turc (1961)
Hargreaves et al (1985)
3. Priestley and Taylor (1972)
4. Penman Monteith
5 calculation methods
5. Energy budget residual
Increasing measurement requirements
Indirect
Partially empirical
Highly uncertain

## Slide 200
Output: Evapotranspiration (ET)
Turc (1961)
Hargreaves et al (1985)
3. Priestley and Taylor (1972)
4. Penman Monteith
5 calculation methods
5. Energy budget residual
Available August 2004 -
Available September 1994 -

## Slide 201
Calculated ET April 22-23, 2005
ET (mm/hr)
Day
Empirical
Energy-based
Low
High
Turc x 2 close to energy budget.
Energy budget most accurate.

## Slide 202
BG1 and BG2 are “Weather Measure” 193 mm accumulators.
Gauges do not differ by more than 0.02 inches in any storm

## Slide 203
RBG1 – Hydrologic Services TB3 200 mm 0.2 mm/tip tipping bucket gauge.
Plots 1 and 2 (P1 and P2).

## Slide 204
BG2 is the reference rain gauge.

## Slide 205
Prof Jim Dooge
(1922 - 2010)
wise counsel and friend
Supervising SJB
RG2 reference
gauge - April 2001
International Hydrology Prize: Dooge Medal
Named to honor Jim in 2014

## Slide 206
Tipping bucket gauge (calibrated) annually.
Installed August 1994.
Not recommended.
Gauges installed as “checks” in later years.

## Slide 207
2003 measured cumulative fluxes
Benchmark rain
January 1
May 31
Rain undercatch
Bias

## Slide 208
2003 measured cumulative fluxes
Benchmark rain
Most rain becomes subsurface flow
More water lost to ET
January 1
May 31

## Slide 209
2003 measured and modeled cumulative fluxes
Benchmark rain
Turc
Turc x 2
ET: S-Wave radiation, Temperature, R-H; Turc, 1961

## Slide 210
2003 measured and modeled cumulative fluxes
Benchmark rain
HYDRUS modeled flow
19%

## Slide 211
2003 measured and modeled cumulative fluxes
Benchmark rain
Modeled flow
Bias

## Slide 212
Use of biased wind affected rain catch and low potential ET yielded approximately the correct cumulative hydrograph.
Modern methods of model parameter estimation would have used these typically available erroneous signals to determine hillslope hydraulic properties.

## Slide 213
Any such calibrated model would yield approximately the “right answer” concerning streamflow representation but have completely wrong soil water properties.
Such a model would be unsuitable (and indefensible) for prediction of changed “land-use” or for changed inputs, e.g. climate change.

## Slide 214
The TB3 pit gauge’s under-catch results from funnel airflow restrictions in the siphon delivery system in gusty storms.
This is documented in Kampf and Burges, J of Hydrology, 2010.

## Slide 216
Landmark technological developments 1944 -
Follow up technology
Issues in hydrology and water resources engineering
The importance of mentors
Choosing research topics
Take home message

## Slide 217
Unknown time-varying biases and stochastic errors in precipitation and potential ET cannot be corrected or represented by any plausible Bayesian prior distributions.
There is no substitute for accurate model input time series.
Rain gauge under catch has been known for many years, e.g. John Rodda, Wallingford, UK

## Slide 218
Rodda, J. C. (1967) - The rainfall measurement problem. Proc. IAHS Gen. Ass. Bern, IAHS Pub, (78), 215-231

## Slide 219
1 ft.

## Slide 220
Under catch about 8%

## Slide 221
We can make substantial progress by putting in place hydrologically useful rain measuring networks. (e.g., Sieck, Burges and Steiner, WRR, 2007.

## Slide 223
We must make substantially improved measurements from which we can determine unbiased evaporative fluxes.

## Slide 224
Study excellent work from the past.
I recommend that you read the technical reports of the Miami Conservancy District, published 102 years ago.
There is exceptional scholarship in these reports; we can all gain insights from them.

## Slide 225
Three papers that offer guidance for improving hydrologic measurement and modeling.

## Slide 226
2020

## Slide 227
2021

## Slide 228
2021
This discussion focuses mostly on conceptual and physical/process-based models where understanding the internal catchment processes and hydrologic pathways is important.
Such hydrological models can be improved by using data from advanced remote sensing (both spatial and temporal) and derivatives, applications of machine learning, flexible structures, and informing models through nested catchment studies in which internal catchment processes are elucidated.

## Slide 229
Nature, 2021

## Slide 230
Nature, 2021
Temporal and spatial patterns of bedrock water use across the continental United States indicate that woody plants extensively access bedrock water for transpiration.
Important to include in models

## Slide 231
Water for food, now and in the future:
March 2024 UNESCO report

## Slide 232
Launch of the 2024 UN World Water Development Report: Water for Prosperity and Peace

## Slide 233
This is an exciting time for research and professional practice in hydrology and water resources engineering.
There is much work to be done.
It is essential that accurate measurements be used.

## Slide 235
Sylvia and Steve - Odoray Grand View - Yoho National Park, September 9, 2023, Macarthur Lake, background right.

## Slide 236
References:
Kampf, Stephanie K., Towards Improved Representation of Hydrologic Processes: Linking Integrated and Distributed Hydrologic Measurements to a Physically-Based Model for a Planar Hillslope Plot, Water Resources Series Technical Report No. 183, Dept. of Civil and Environmental Engineering, University of Washington, 214p, 2006.
Kampf, S. K. and S. J. Burges, A framework for classifying and comparing distributed hillslope and catchment hydrologic models, Water Resour. Res., 43, W05423, doi:10.1029/2006WR005370, 2007.
Kampf, S. K. and S. J. Burges, Parameter estimation for a physics-based distributed hydrologic model using measured outflow fluxes and internal moisture states, Water Resour. Res., 43, W12414, doi: 10.1029/2006WR005605, 2007.

## Slide 237
Kampf, S. K., and S. J. Burges, Quantifying the water balance in a planar hillslope plot: effects of measurement errors on flow prediction, Journal of Hydrology, 380 191-202, DOI:10.1016/j.jhydrol.2009.10.036, 2010.
Kampf, S. K., Burges, S. J., Hammond, J. C., Bhaskar, A., Covino, T. P., Eurich, A., et al. (2020). The case for an open water balance: Re‐envisioning network design and data analysis for a complex, uncertain world. Water Resources Research, 56, e2019WR026699. https:// doi.org/10.1029/2019WR026699
Sieck, L. C., S. J. Burges, and M. Steiner, Challenges in obtaining reliable measurements of point rainfall Water Resour. Res., 43(1),W0142010.1029/2005WR004519, 2007.

## Slide 238
Šimùnek, J., M. Sejna, M. Th. van Genuchten, The HYDRUS-2D software package for simulating two-dimensional movement of water, heat, and multiple solutes in variably saturated media, in International Ground Water Modeling Center, Colorado School of Mines, Golden, Colorado, 1999.
Šimùnek, J., Nick J. Jarvis, M. Th. van Genuchten, Annemieke Gardenas, Review and comparison of models for describing non-equilibrium and preferential flow and transport in the vadose zone. Journal of Hydrology 272:14-35, 2003.

## Slide 240
Technical reports of The Miami Conservancy District
Available at:
https://depts.washington.edu/sjbx/
Download file "MCD Reports.zip"
There are ten reports starting in 1917 and ending in 1922. There is an updated version of Report V (Rainfall) published in 1936. I did not know about this report until I requested all the reports from our UW Library. I scanned in its entirety the 1936 report (it is the largest file). The other ten reports were all scanned initially by Google. I found numerous badly copied, unreadable, and missing pages (particularly fold out figures). I copied and replaced such pages in all the reports. I was restricted to copying from bound copies of the reports hence a few pages are a bit out of alignment. The pages I scanned are all at 300 dpi. I found this necessary to ensure that dimensions on figures etc., were readable.
I have also included scans of two figures and a location map. I do not know from which report they were extracted; my source was pages at the end of a single bound copy of reports 1-V.
I have also included a copy of a 1928 paper by Arthur Morgan. That paper provides essential background about how he located his top engineers and their experience coming to the Miami Valley flood problem.

## Slide 241
Reading Guide - Extreme Flood Issues and System Design:
1. Burges-Water Systems Planning-ASCE-WRPM-1979 pages 98-100 for a brief coverage of The Miami Conservancy District flood mitigation work.
2. “Storm Rainfall of Eastern United States - The Engineering Staff - Miami Conservancy District Technical Reports Part V, 1917” for investigations to determine major flood producing rain.
Recommended initial reading: Chapter XI (page 241) and then Chapter XII (page 268).
There was a follow up to Report V published in 1936 (“Storm Rainfall of Eastern United States - The Engineering Staff - Miami Conservancy District Technical Reports Part V, Rev 1936-sjb”) that included 20 more years of data. See: Chapter 1 pages 1 - 5.
3. “Hydraulics of the Miami Flood Control Project - Sherman M. Woodward - Miami Conservancy District - Technical Reports Part VII, 1920” for details of the actual design. Most notable are Chapters XII and XIII. This was exceptional water resources engineering.

## Slide 244
Berlin airlift
Berlin Blockade (24 June 1948 – 12 May 1949)
Only access to West Berlin was by aircraft
One of the first major international crises of the Cold War

## Slide 246
Berliners watching a C-54 land at Tempelhof Airport (1948) – all food and fuel (coal) for West Berlin’s 2.4 million people was brought in by air
https://en.wikipedia.org/wiki/Berlin_Blockade
Courageous aircrews and heroic logistical and rapid airport runway construction (and maintenance) feats.

## Slide 247
Coal Deliveries - peak 1-day rate
Noon April 15, to Noon April 16, 1949 12,941 tons of coal delivered by 1,383 flights without accident.
Total delivery for April, 1949 234,476 tons.
https://en.wikipedia.org/wiki/Berlin_Blockade

## Slide 248
Major societal concerns

## Slide 249
Fig. 28. How much richer would the world have been had we solved certain issues, 1900–2050 (Lomborg 2013). The estimate for each problem shows how much richer the world could have been had this problem been addressed (so can add to more than 100%). For reference, how much richer the world would be if we didn't have global warming (the cost in percent of global GDP of Nordhaus optimal 3.5°C scenario, 2015–2100).
Lomborg, Bjorn, Welfare in the 21st century: Increasing development, reducing inequality, the impact of climate change, and the cost of climate policies, Technological Forecasting & Social Change, 2020

## Slide 250
Fig. 28. How much richer would the world have been had we solved certain issues, 1900–2050 (Lomborg 2013). The estimate for each problem shows how much richer the world could have been had this problem been addressed (so can add to more than 100%). For reference, how much richer the world would be if we didn't have global warming (the cost in percent of global GDP of Nordhaus optimal 3.5°C scenario, 2015–2100).
Lomborg, Bjorn, Welfare in the 21st century: Increasing development, reducing inequality, the impact of climate change, and the cost of climate policies, Technological Forecasting & Social Change, 2020

## Slide 251
Fig. 28. How much richer would the world have been had we solved certain issues, 1900–2050 (Lomborg 2013). The estimate for each problem shows how much richer the world could have been had this problem been addressed (so can add to more than 100%). For reference, how much richer the world would be if we didn't have global warming (the cost in percent of global GDP of Nordhaus optimal 3.5°C scenario, 2015–2100).
Lomborg, Bjorn, Welfare in the 21st century: Increasing development, reducing inequality, the impact of climate change, and the cost of climate policies, Technological Forecasting & Social Change, 2020

## Slide 252
Fig. 28. How much richer would the world have been had we solved certain issues, 1900–2050 (Lomborg 2013). The estimate for each problem shows how much richer the world could have been had this problem been addressed (so can add to more than 100%). For reference, how much richer the world would be if we didn't have global warming (the cost in percent of global GDP of Nordhaus optimal 3.5°C scenario, 2015–2100).
Lomborg, Bjorn, Welfare in the 21st century: Increasing development, reducing inequality, the impact of climate change, and the cost of climate policies, Technological Forecasting & Social Change, 2020

## Slide 253
Fig. 28. How much richer would the world have been had we solved certain issues, 1900–2050 (Lomborg 2013). The estimate for each problem shows how much richer the world could have been had this problem been addressed (so can add to more than 100%). For reference, how much richer the world would be if we didn't have global warming (the cost in percent of global GDP of Nordhaus optimal 3.5°C scenario, 2015–2100).
Lomborg, Bjorn, Welfare in the 21st century: Increasing development, reducing inequality, the impact of climate change, and the cost of climate policies, Technological Forecasting & Social Change, 2020

## Slide 254
Major developments in computer programing languages
See: History of programming languages – Wikipedia
1951 – Regional Assembly Language
1952 – Autocode
1954 – IPL (forerunner to LISP)
1955 – FLOW-MATIC (led to COBOL)
1957 – FORTRAN (first compiler)
1957 – COMTRAN (precursor to COBOL)
1958 – LISP
1958 – ALGOL 58
1959 – FACT (forerunner to COBOL)
1959 – COBOL
1959 – RPG
1960 – ALGOL 60

## Slide 255
1962 – APL
1962 – Simula
1962 – SNOBOL
1963 – CPL (forerunner to C)
1964 – Speakeasy
1964 – BASIC
1964 – PL/I
1966 – JOSS
1966 – MUMPS
1967 – BCPL (forerunner to C)
1967 – Logo (an educational language that later influenced Smalltalk and Scratch)

## Slide 256
1990 – Haskell
1990 – Python
1991 – Visual Basic
1993 – Lua
1993 – R
1994 – CLOS (part of ANSI Common Lisp)
1995 – Ruby
1995 – Ada 95
1995 – Java
1995 – Delphi (Object Pascal)
1995 – Visual FoxPro
1995 – JavaScript
1995 – PHP
1996 – OCaml
1997 – Rebol

## Slide 278
GRACE up to June 2017

## Slide 279
NASA Earth Fleet – June 2021
LANDSAT – 9 Launched September 27, 2021

## Slide 280
NASA Earth Fleet – December 2023

## Slide 282
A Personal Journey - Fifty-seven Years Working in Hydrology and Water Resources Engineering
Stephen J. (Steve) Burges
Professor Emeritus
Department of Civil and Environmental Engineering
University of Washington, Seattle, WA
CEE 500 Seminar
230 More Hall, University of Washington
April 11, 2024

## Slide 283
Some Lessons Learned From Fifty-seven Years Working in Hydrology and Water Resources Engineering
Stephen J. (Steve) Burges
Professor Emeritus
Department of Civil and Environmental Engineering
University of Washington, Seattle, WA
CEE 500 Seminar
230 More Hall, University of Washington
April 11, 2024

## Slide 284
A Personal Journey - Working in Hydrology and Water Resources Engineering for Fifty-seven Years
Stephen J. (Steve) Burges
Professor Emeritus
Department of Civil and Environmental Engineering
University of Washington, Seattle, WA
CEE 500 Seminar
230 More Hall, University of Washington
April 11, 2024

## Slide 286
LASER - Light Amplification by Stimulated Emission of Radiation
Theodore Maiman
built first functional laser
- May 16, 1960

## Slide 287
Stimulated Optical Radiation in Ruby, T. H. Maiman, Nature 187, 493–494, 1960

## Slide 289
< 3/4 Page !

## Slide 290
Stimulated Optical Radiation in Ruby, T. H. Maiman, Nature 187, 493–494, 1960
"probably more important per word than any of the papers published by Nature over the past century.“
Obituary - Theodore H. Maiman (1927–2007), Charles Townes, Nature, 2007.
Dr Townes shared the 1964 Nobel Prize in Physics for inventing the LASER and MASER

## Slide 292
An integrative framework for much of hydrologic science has been provided by focusing on the “Critical Zone”, first introduced in:
“Basic Research Opportunities in Earth Science”, National Research Council, p 154, 2001
I am guilty, together with Professor Gail Ashley (Rutgers) and the late Professor Larry Wilding (Texas A & M), for introducing this framework to the NRC Committee.

## Slide 294
Critical zone
Heterogeneous, near-surface environment in which complex interactions involving rock, soil, water, air, and living organisms regulate the natural habitat and determine the availability of life-sustaining resources.

## Slide 295
Critical Zone

## Slide 296
Relative scales
Earth = 1 m
Mt Everest = 0.7 mm
Mariana Trench = 0.9 mm
Critical zone
Little known about the 1 m domain
Our domain is -0.1 to 0.7 mm above sea level

## Slide 297
Critical zone scales
km

## Slide 299
Oroville Dam, CA, failed spillway, Feb 27, 2017
https://en.wikipedia.org/wiki/Oroville_Dam#/media/File:Oroville_Dam_spillway_damage_27_Feb_2017.jpg
Cost of replacement of spillway 2017-2018 and stabilization below emergency spillway – 2018, $1.2B (DWR Feb. 2021)
FEMA pays $630 Million

## Slide 300
Emergency spillway -1,730 ft. long - for uncontrolled release of floods up to PMF
March 2017
Earth dam – 6,920 ft. long
Discharge – Failed Chute Spillway

## Slide 301
March 2017
Back cutting at 10 ft./hour
Damage from use of emergency spillway

## Slide 303
Early work – responding to short-term needs of regulatory agency colleagues
1. Washington State, Department of Ecology

## Slide 304
Uses water quality models formulated as Extended Kalman Filters ( a major new tool) and statistical power tests.
We chose the wrong journal.
This work has eluded the research community!
ASCE

## Slide 305
Dennis and I chose the appropriate journal.
This work has been used and cited extensively.

## Slide 307
2021

## Slide 312
Landmark technological developments 1944 -
Follow up technology
Issues in hydrology and water resources engineering
The importance of mentors

## Slide 313
What possibilities exist for using “machine Learning” for predicting hydrologic response from “ungauged catchments”?

## Slide 314
Nature – March 20, 2024.
AI skill measures used:
Precision
Recall
F1 Score

## Slide 315
Here we show that artificial intelligence-based forecasting achieves reliability in predicting extreme riverine events in ungauged watersheds at up to a five-day lead time that is similar to or better than the reliability of nowcasts (zero-day lead time) from a current state-of-the-art global modelling system (the Copernicus Emergency Management Service Global Flood Awareness System).

## Slide 317
2004

## Slide 318
2,000- year reconstructed Colorado River annual flow volume
Long time series records are need to establish trends

## Slide 320
Water for food, now and in the future:
March 2024 UNESCO report

## Slide 321
Launch of the 2024 UN World Water Development Report: Water for Prosperity and Peace

## Slide 322
From Report, Page 3.
Since 1961, the area under irrigation more than doubled, from 139 million ha to over 328 million ha in 2018
About 40% of global agriculture production comes from irrigated land, which is only about 20% of all agricultural land

## Slide 323
Irrigation plays a critical role in the transition from subsistence to commercial farming, poverty alleviation and economic growth.
Irrigated yields tend to be 30–100% higher
compared to adjacent rainfed areas.

## Slide 324
More than 3 billion people live in agricultural areas with high or very high levels of water shortages or water scarcity.
The impacts of climate change are expected
to aggravate this situation, with repercussions for agri-food systems and human health, among others.

## Slide 325
From Report, Page 7.
Transboundary cooperation
Transboundary rivers, lakes and aquifers account for 60% of the world’s freshwater flows.
Over 310 river basins and an estimated 468 aquifers are shared between two or more countries.
153 countries share rivers, lakes and aquifers.

## Slide 326
Transboundary waters globally face significant and increasing pressures due to
population increase,
growing water demands,
ecosystem degradation
and climate change.

## Slide 327
Unsustainable irrigation expansion for food production

## Slide 328
March 2024

## Slide 329
March 2024
We found that more than half (52%) of the irrigation expansion has taken place in areas that were already water-stressed in the year 2000, with India alone accounting for 36% of global unsustainable expansion.

## Slide 330
Major mid-career influence:
Nobel Laureate Sir Peter Medawar’s book “Pluto’s Republic”, 1982 - first read January 1993 - extract from his essay on induction:
"I reckon that for all the use it has been to science about four-fifths of my time has been wasted, and I believe this to be the common lot of people who are not merely playing follow-my-leader in research".
If only about 20 % of Sir Peter’s research was productive, the rest of us would be doing well if 5% of ours was potentially valuable.

## Slide 333
Subjects included:
Canals and Waterborne Transportation (Erie Canal)
Complex Water Supply System (New York City)
Flood Mitigation Planning (Miami Conservancy District)
Irrigated Agriculture in the West (Colorado River System – Hoover Dam)
Multiple Purpose Systems (Tennessee Valley Authority - TVA)

## Slide 335
Science, March 2024