Equipment Checklists

All equipment must be used for the purpose for which it was designed.

Infant Scale Checklist

A scale for weighing infants should have a large enough tray to support the infant and weigh to 20 kg or 40 lb.

- High quality beam balance or electronic digital

- Weighs to 20 kg or 40 lb

- Weighs in 0.01 kg (10 gm) or 1/2 oz increments

- Tray large enough to support the infant

- Can be easily ‘zeroed’ and checked

- Weight can be ‘locked’ in

- Can easily be ‘tared’ to zero

- Can be read at ‘eye level’ of measurer

- Can be calibrated

- Motion detector and stabilizer

- No length device attached

Infant Lengthboard Checklist

Length boards for infants must be sturdy, easily cleaned and specific to the purpose and has:

- A firm, inflexible, flat horizontal surface with a measuring tape in 1 mm (0.1 cm) or 1/8 inch increments

- Tape is stable and easily read

- An immovable headboard at a right angle to the tape

- A smoothly moveable footboard, perpendicular to the tape

Head Circumference Tape Checklist

- Non-stretchable, plasticized

- 1/4 -1/2 inch wide

- Insertion tape in 0.1 cm or 1/8 inch increments

Child and Adolescent Scale Checklist

A scale for weighing children & adolescents should be stable, in a ‘private’ location, and:

- High quality beam balance or electronic digital

- Weighs in 0.1 kg (100 gm) or 1/4 lb increments

- Weight can be ‘locked’ in

- Weight is read at ‘eye level’ of measurer

- Stable weighing platform

- Can be easily ‘zeroed’

- Can be calibrated

# No stature device attached

- No wheels on scale

- Handpost attached to base of scale

Child and Adolescent Stadiometer Checklist

Stadiometers must be stable, calibrated and dedicated to the purpose.  This requires:

- A vertical board with an attached metric rule

- An easily moveable horizontal headboard that can be brought into contact with the most superior part of the head

- A wide and stable platform or firm uncarpeted floor as the base

- Firmly mounted on a stable wall

- Easily read, stable tape or digital readout in 0.1 mm or 1/8 inch increments