# Air Sampling Study of the 2000 Montana Wildfire Season

Paper # 1131

Tony J. Ward and Garon C. Smith

# The University of Montana – Missoula, MT, Department of Chemistry, 59812

## ABSTRACT

The wildland fires of 2000 comprised one of the most severe fire seasons in U.S. history, and had a direct impact on the city of Missoula, Montana.  This paper presents the results of chemical sampling conducted before, during, and after the 2000 fire season in Missoula, Montana, and provides a detailed characterization of particulate and chemical emissions from extensive wildland fires.  We summarize levels of PM2.5, trace elements (13 - 82), anions (fluoride, chloride, nitrate, and sulfate), cations (ammonium, magnesium, calcium, potassium, and sodium), Organic Carbon (OC), Elemental Carbon (EC), and Total Carbon (TC) collected on the PM2.5 filters.  We also quantified 61 semi-volatile organic compounds (SVOCs) and 54 volatile organic compounds (VOCs).  In addition to the Chemical Mass Balance (CMB) sampling, particulate information collected by the Montana Department of Environmental Quality is provided.  This includes PM2.5 data collected every 3 days in Missoula and Hamilton (46 miles south) throughout the fire season.

Missoula is located in the Rocky Mountains of western Montana at an elevation of 3,200 feet.  With a population of over 70,000 inhabitants, Missoula is the largest urban area in the United States completely surrounded by the Rocky Mountains.  During the 2000 fire season, an ongoing project conducted by The University of Montana, Department of Chemistry, was already collecting samples for a CMB study to identify the sources of air pollution in the Missoula Valley.  This sampling study focuses on PM2.5, VOCs, and SVOCs.

### INTRODUCTION

The Missoula Valley has traditionally experienced problems with air pollution as a result of its topographic constraints and lack of air dispersion.  On March 22, 2000, a yearlong sampling project began with the objective of identifying the sources of air pollution in the Missoula Valley.  During the summer, record-low fuel moisture and persistently hot, dry weather caused drought conditions throughout much of the West.   The fire season began early, became intense, and lasted well into the fall.  Until the end of August, fire activity was focused mostly in Idaho and Montana where more than half of the nation’s fires were burning.  Several wildfires were burning in close proximity to Missoula during the summer of 2000.  Approximately 60 miles to the south, the Sula Complex, Valley Complex, and the Blodgett Canyon fires burned in the Bitterroot mountains.  About an hour to the west, the Flat Creek Complex, Clear Creek, and Ninemile Divide Complex fires burned.  Frequently, smoke moved downwind directly into the Missoula Valley filling it up.  Accumulations of smoke in the city led to nine Stage 1 and five Stage 2 air alerts.  The local Air Pollution Control Board had to enact an emergency order to help industry avoid unnecessary shut downs and schools to adjust outdoor athletic activities. Just before Labor Day, rain, cooler temperatures, and higher humidity finally came to the Northern Rockies ending the 2000 wildfire season.

The statistics from the 2000 wildfire season are staggering.  From January through the end of October, wildland fires burned 6,966,995 acres across the United States.  In Montana and Idaho alone, more than 4000 fires burned an estimated 2.2 million acres.  With fire fighting assistance from Australia, New Zealand, Canada, Mexico, and six battalions of the military, fire suppression costs through October totaled an estimated $877,847,296.1,2

Smoke is composed of a complex mixture of particles, liquids, and gaseous compounds.  These include carbon monoxide, hydrocarbons, particulate matter, nitrogen oxides (NOx), sulfur oxides (SOx), oxidants (including small amounts of ozone), and polycyclic organic material.  Carbon monoxide (CO) is the most abundant air pollutant emitted from burning wildland fuels.  Coupled with carbon dioxide (CO2) and methane (CH4), CO emissions from fires have been found to be a significant source of greenhouse gases.3  Hydrocarbons, including ethylene, alkynes, aldehydes, furans, and carboxylic acids, are products of incomplete combustion.  Particulate matter, comprised of a complex mixture of soot, tars, and volatile organic substances, is another major component of smoke.4  NOx and SOx are found in smaller concentrations.  Some NOx forms at lower temperatures, but the amount of NOx produced depends primarily on the nitrogen content of the fuels burned by the fire.5,6  SOx are usually produced in negligible quantities because forest fuels generally have a low sulfur content.7

Fires also emit a large number of organic compounds which are partitioned between the gaseous and liquid or solid phase at ambient temperatures.  These are called semi-volatile organic compounds (SVOCs).  An important class of SVOCs are polycyclic aromatic hydrocarbons (PAHs), which are significant because many of its members are carcinogenic.  PAHs can condense or be adsorbed onto the surface of fine particles.  They are assembled from carbon fragments into larger structures in low-oxygen environments, such as occurs inside the flame envelope in the fuel-rich region of the flame structure.8  Little characterization work has been done from fires on these compounds.9

Most of the things known about smoke come from either research conducted with prescribed burns or burns conducted in a controlled laboratory environment.  Because of the logistics and wide variety of compounds emitted from forest fires, it is very difficult to conduct a comprehensive study of the pollutants emitted from wildfires.  Even though we did collect samples during the fire season, PM2.5 speciated samples were collected only every 12 days.  A more comprehensive study would have collected samples every 3 days.  Because of the breadth of analyses performed on each sample, a shorter sampling interval was not feasible.  It is also difficult to determine accurate concentrations of oxygenates from fires without specialized sampling equipment.  Some of these compounds when captured on solid media often transform from reactive species to more stable forms.10,11

EXPERIMENTAL METHODS

Samples were collected at two locations every 12 days during the fire season for a CMB source apportionment study.  Boyd Park is an established sampling site on the east side of the Missoula Valley maintained by the Montana Department of Environmental Quality (DEQ) for PM10 and PM2.5 compliance monitoring.  Frenchtown is located 27 km away on the west side of the Missoula Valley.  In addition to the CMB sampling at both sites, the Frenchtown site also collected VOC and SVOC samples every 6 days.  During sampling, five samplers ran simultaneously at each of the two monitoring sites:  two PM2.5 samplers (one with a quartz filter and the other with a Teflon filter), one PUF (polyurethane foam) sampler, and two VOC samplers.  The following analyses were conducted on the PM2.5 filters:  gravimetric, trace elements, anions, cations, Total Carbon (TC), Organic Carbon (OC), and Elemental Carbon.  SVOC and VOC analyses were conducted by Gas Chromatography / Mass Spectrometry (GC/MS) at The University of Montana laboratory.

PM2.5 Sampling

PM2.5 sampling was conducted every 12 days.  During each CMB sampling event at Boyd Park and Frenchtown, two PM2.5 samplers ran simultaneously over a 24-hour time period starting at midnight and ending at midnight the next day.  The Missoula Valley Sampling Program (as well as Montana DEQ monitoring) utilize the BGI PQ200 Ambient PM2.5 Federal Reference Method (FRM) Sampling Systems.

Because all analyses cannot be conducted on a singular type of filter media, one PM2.5 sampler collected samples on a quartz glass filter and the other PM2.5 sampler on a Teflon filter.  All PM2.5 filters (both quartz glass and Teflon) were supplied by Chester LabNet (Tigard, Oregon).

PM2.5 Analyses

All PM2.5 filter samples were sent to Chester LabNet for analyses.  In conducting the gravimetric analysis, the Teflon filters were weighed before and after sampling to compute the mass of captured particulates.  Results were presented in micrograms ((g) per filter.  Protocol Number 5 was used in determining concentrations of trace elements with atomic numbers of 13 – 82 by photon-induced X-ray fluorescence (XRF).  The following trace elements were quantified from the Teflon filters:

aluminum		titanium	  copper		strontium	indium

silicon		vanadium	  zinc		yttrium	tin

phosphorus	chromium	  gallium		zirconium	antimony

sulfur		manganese	  arsenic		molybdenum   barium

chlorine		iron		  selenium	palladium	lanthanum

potassium		nickel	  bromine		silver	mercury

calcium		cobalt	 	  rubidium	            cadmium	lead

germanium

Using EPA Methods 300.0 and 200.7, the PM2.5 quartz glass filters were analyzed by ion chromatography (IC) for anions (fluoride, chloride, nitrate, and sulfate) and cations (ammonium, magnesium, calcium, potassium, and sodium).  The Thermal/Optical Reflectance (TOR) method was used by Chester LabNet in performing the OC, EC, and TC analyses.

###### PUF Sampling

In addition to the two PM2.5 samplers installed at Boyd Park and Frenchtown, a Polyurethane Foam (PUF) sampler was installed at each site to collect Total Suspended Particulates (TSP) and SVOCs during sampling.  Sampling was conducted over the same 24-hour time period as PM2.5 sampling (midnight to midnight) to obtain average daily levels of airborne pollutants.  PUF sampling at Frenchtown was conducted every 6 days while PUF sampling was conducted every 12 days at Boyd Park.  Two Andersen Model GPS1-1 PUF Hi-Vol Sampling Systems were used to collect airborne particles.

##### PUF Analyses

All PUF analyses were conducted at The University of Montana laboratory.  The PUF filter and plug were subjected to solvent extraction in a Soxhlet apparatus using a combination of diethyl ether and hexane.  The extract was concentrated in a Kuderna-Danish (K-D) evaporator prior to analysis by Gas Chromatography / Mass Spectrometry (GC/MS).  A suite of 61 organic contaminants were quantified:

Phenol				Bis-(2-chloroethyl) ether	2-Chlorophenol

1,3-Dichlorobenzene 		1,4-Dichlorobenzene 		1,2-Dichlorobenzene

2-Methylphenol 		Bis-(2-chloroisopropyl) ether 	4-Methylphenol

N-Nitrosodi-n-propylamine	Hexachloroethane 		Nitrobenzene

Isophorone 			2-Nitrophenol 			2,4-Dimethylphenol

Bis-(2-chloroethoxy) methane	2,4-Dichlorophenol		1,2,4-Trichlorobenzene Naphthalene			4-Chloroaniline			Hexachlorobutadiene

4-Chloro-3-methylphenol	2-Methylnaphthalene		Hexachlorocyclopentadiene 2,4,6-Trichlorophenol		2,4,5-Trichlorophenol		2-Chloronaphthalene

2-Nitroaniline			Dimethyl phthalate 		Acenaphthylene

3-Nitroaniline 			Acenaphthene			4-Nitrophenol

Dibenzofuran			2,4-Dinitrotoluene 		Diethyl phthalate

4-Chlorophenyl phenyl ether 	Fluorene			4-Nitroaniline

2-Methyl-4,6-dinitrophenol 	Azobenzene 			4-Bromophenyl phenyl ether

Hexachlorobenzene 		Pentachlorophenol 		Phenanthrene

Anthracene 			Carbazole 			Di-n-butyl phthalate

Fluoranthene 			Pyrene 				Butyl benzyl phthalate

Benzo(a)anthracene 		Bis (2-ethylhexyl) phthalate 	Chrysene

Di-n-octyl phthalate 		Benzo(b)fluoranthene 		Benzo(k)fluoranthene

Benzo(a)pyrene 		Indeno(1,2,3-cd)pyrene		Dibenzo(a,h)anthracene Benzo(ghi)perylene

Analyte separations were accomplished on a Hewlett Packard GCD 5890 series II Gas Chromatograph, 5973 Mass Spectrometer (GC/MS) with a 0.32 mm ID X 30.0 meter Restek XTI-5 column.  Sample extracts were analyzed using the following temperature program:

Inlet Temperature:		220 (C		Detector Temperature:		270 (C

Injection Mode:			Splitless		Initial Oven Temperature:		40 (C

Initial Oven Hold:		4.0 minutes	Oven Ramp Rate 1:		10 (C / minute

Oven Ramp Final Temp 1:		300 (C 		Oven Ramp Rate 1 Final Time:	5.0 minutes

Oven Ramp Rate 2:		10 (C / minute	Oven Ramp Final Temp 2:		330 (C

Oven Ramp Rate 1 Final Time:	2.0 minutes	Total Run Time:			40.0 minutes

Carrier Gas:			Helium		Flow:				1.0 ml/min

Sampling efficiencies were tracked by spiking the samples with field surrogates (d10–fluoranthene and d12-benzo[a]pyrene) prior to sampling.  Laboratory surrogate standards (d10 -fluorene and d10–pyrene) were spiked onto the sample before extraction to track the analysis efficiencies.  Analytes were quantified using the following internal standards:  d8 –naphthalene, d10 –acenaphthene, d10 –phenanthrene, d12 –chrysene, and d12 –perylene.   A decafluorotriphenylphosphine (DFTPP) sample was analyzed daily to document that the GC/MS met tuning and standard mass spectral abundance criteria prior to the analysis of any calibration standards or field samples.

PAHs were quantified according to US EPA Method TO-13A, 1999:  Compendium of Methods for the Determination of Toxic Organic Compounds in Ambient Air.  Second Ed.  Determination of Polycyclic Aromatic Hydrocarbons (PAHs) in Ambient Air Using Gas Chromatography / Mass Spectrometry (GC/MS).12

VOC Sampling

To capture VOCs with molecular weights smaller than 250 g/mol, constant flow air sampling pumps with sorbent tubes were used at both the Boyd Park and Frenchtown sites.  SKC Model 222-3 (Eighty Four, PA) low-flow air sampling pumps actively sampled ambient air through Supelco Carbotrap( 300 multibed sorbent tubes.

VOCs were quantified according to US EPA Method TO-2, 1984:  Method for the Determination of Volatile Organic Compounds in Ambient Air by Carbon Molecular Sieve Adsorption and Gas Chromatography / Mass Spectrometry (GC/MS).  Revision 1.0, April, 1984.13

VOC Analyses

Exposed sample tubes were brought to The University of Montana laboratory for analysis.  The standard EPA suite of 54 VOCs were quantified:

Supelco Mix 1			Supelco Mix 2			Supelco Mix 3

Chlorobenzene			Benzene			cis-1,3-Dichloropropene

Isopropylbenzene		Bromobenzene			Hexachlorobutadiene

n-Propylbenzene		Ethylbenzene			trans-1,3-Dichloropropene

1,2-Dimethylbenzene		1,4-Dimethylbenzene		Trichloroethene

1,4-Dimethylbenzene		n-Butylbenzene			1,1-Dichloropropene

sec-Butylbenzene		Naphthalene			1,1,1,2-Tetrachloroethane

tert-Butylbenzene		Isopropyltoluene		1,1,2-Trichloroethane

1,2-Dichlorobenzene 		Styrene 			1,1,2,2-Tetrachloroethane

1,3-Dichlorobenzene 		Toluene			1,2-Dibromo-3-chloropropane

1,4-Dichlorobenzene		1,2,3-Trichlorobenzene		1,2-Dibromoethane

2-Chlorotoluene		1,2,4-Trichlorobenzene		1,2-Dichloroethane

4-Chlorotoluene		1,2,4-Trimethylbenzene		1,2-Dichloropropane

1,3,5-Trimethylbenzene 	1,2,3-Trichloropropane

1,3-Dichloropropane

Supelco Mix 4			Supelco Mix 5

Bromochloromethane		Bromodichloromethane

Tribromomethane 		cis-1,2-Dichloroethene

Tetrachloromethane		Dibromochloromethane

Trichloromethane 		Dichloromethane

Dibromomethane		trans 1,2-Dichloroethene

Tetrachloroethene		1,1-Dichloroethane

1,1-Dichloroethene

1,1,1-Trichloroethane

2,2-Dichloropropane

Release of the sorbed chemicals was affected on a Dynatherm MTDU Model 910 thermal desorption unit.  A Model 900 ACEM sample concentrator was used to focus the samples prior to injection into the Hewlett Packard 6890 series Gas Chromatograph with Restek RTX502.2 capillary column (60m, 0.32mm ID).  Quantitation was performed on a 5973 Mass Spectrum Detector (MSD).  The following program parameters were used for VOC analysis by GC/MS:

Inlet Temperature:		220 (C		Detector Temperature:		270 (C

Injection Mode:			Split		Split Flow:			9.9 ml/min

Split Ratio:			10:1		Total Flow:			13.0 ml/min

Initial Oven Temperature:		40 (C		Initial Oven Hold:		5.0 minutes

Oven Ramp Rate:			5 (C / minute	Oven Final Temperature:		220 (C

Oven Final Time:			9.0 minutes	Total Run Time:			50.0 minutes

Carrier Gas:			Helium		Flow:				1.0 ml/min

Dynatherm MTDU Model 910 Parameters

Interface Temperature:		120 (C 		Transfer Line Temp:		120 (C

Interface Idle Temperature:	40 (C		Transfer Line Idle Temperature:	40 (C

Tube Desorb Temperature:	250 (C		Auxillary Temperature:		NA

Tube Purge Time:		4.0 minutes	Tube Heat Time:			10 minutes

Tube Cool Time:			6.0 minutes	Auxillary Time:			NA

Sample Flow:			100 ml/min	Sample Tube Purge / Desorb Flow:	25.0 ml/min

Gas:				Helium

ACEM Model 900 Parameters

Valve Temperature:  		150 (C		Transfer Line Temperature:	225 (C

Tube Desorb Temperature:	290 (C		Trap Desorb Temperature:		310 (C

Tube Idle Temperature:  		40 (C		Trap Idle Temperature:  		40 (C

Ext. Sample Time:		20 minutes	Tube Dry Time:  			4 minutes

Tube Heat Time:			12 minutes	Tube Cool Time:			4 minutes

Trap Heat Time:			6 minutes	Sys. Recycle Time:		10 minutes

Gas:				Helium

An internal standard mixture of fluorobenzene, 4-bromofluorobenzene, and 1,2-dichlorobenzene-d4 was used to assure quantification of analytes.14  Bromofluorobenzene (BFB) was analyzed at the start of each day to document that the GC/MS met tuning and standard mass spectral abundance criteria prior to standard or field sample analyses.

## Montana DEQ PM2.5 Data

# In addition to the Missoula Valley Sampling Program PM2.5 data, we also present in this paper Montana DEQ PM2.5 compliance data for two sites in Missoula and one site in Hamilton throughout the fire season.  The Montana DEQ maintains two sites in Missoula – one at Boyd Park and the other 3 km north on the roof of the Missoula City/County Health Department.  Data were collected at the three sites every three days throughout the fire season.

# RESULTS AND DISCUSSION

PM2.5

PM2.5 levels reached incredible heights during the 2000 wildfire season in western Montana. We present in Figure 1 the Montana DEQ PM2.5 data for Missoula and Hamilton because they possess a higher temporal resolution (3-days) than the Missoula Valley Sampling Program (12 days). The three traces correspond to the two Missoula sites and the solitary Hamilton site.  The two sites in Missoula showed close agreement in their measurements, consistent with the general observation that PM2.5 levels are fairly homogeneous throughout an airshed.15 For the entire month of August, PM2.5 concentrations were above the annual PM2.5 ambient air quality standard of 15 (g/m3.   On only two occasions did the Missoula sites exceed the 24-hour PM2.5 standard of 65 (g/m3.  On 8/10/00, Boyd Park collected 179.13 (g/m3 and the Health Department collected 165.53 (g/m3.  And on 8/22/00, Boyd Park and the Missoula Health Department collected 82.72 and 90.64 (g/m3, respectively.

In Hamilton, immediately adjacent to the Bitterroot fire complexes, the concentrations were much higher.  In fact, the concentrations were so high that on several occasions the filters became clogged with so much material that the PM2.5 sampler shut down.  The days in which the sampler was overloaded are indicated on Figure 1 by “RL”, which stands for run length (hrs:min).  For the entire month of August, the PM2.5 concentrations were above both the daily and annual PM2.5 ambient air quality standards in Hamilton.

###### Trace Elements

The fires of 2000 emitted a strong fingerprint of potassium and chloride.  Trace elemental data were collected every 12 days at Boyd Park and Frenchtown.  Of the 36 elements analyzed, only 7 showed concentrations above the detection limits during the time period of July 8 – September 30.  These were Al, Si, S, Cl, K, Ca, and Fe.  Only potassium and chloride spiked during the fire season at both Boyd Park (BP) and Frenchtown (Fr).  These data are presented in Figure 2.  Before August, potassium concentrations averaged 0.11 (g/m3 at Boyd Park and 0.07 (g/m3 at Frenchtown.  During August, Boyd Park potassium concentrations were measured at 0.42 and 0.23 (g/m3 on August 13 and 25, respectively.  On August 13 and 25 at Frenchtown, potassium concentrations of 0.27 and 0.32 (g/m3 were measured.  Potassium concentrations dropped back down to baseline levels in September.  The chloride spike was less pronounced.  It was not detected at either site before August.  However, during August, chloride averaged approximately 0.015 (g/m3 at Boyd Park, and 0.01 (g/m3 at Frenchtown.

Chloride levels dropped back down to 0.00 (g/m3 in September with the exception of a 0.01 (g/m3 detected at Frenchtown on September 30.

###### Anions and Cations

No clear signature of the fire season was noted in ionic data.  Ionic data were collected every 12 days during the fire season at both Boyd Park and Frenchtown.  Although there are small trends in some ion concentrations during the fire events, their magnitudes and durations are not as pronounced as other species.  Ionic fluoride and magnesium were not detected during sampling.

###### EC, OC, and TC

All forms of carbon showed a 5- to 6-fold increase in PM2.5 filter samples during the active fire season.  Elemental carbon (EC), Organic carbon (OC) and Total Carbon (TC) data were collected every 12 days at both Boyd Park and Frenchtown.  Figure 3 presents the combined results of Boyd Park (BP) and Frenchtown (Fr) concentrations before, during, and after the fire season.  Before the fire season, Elemental Carbon (EC) averaged approximately 2 (g/m3, Organic Carbon (OC) averaged 8 (g/m3, and Total Carbon (TC) averaged approximately 9 (g/m3 at Boyd Park.  At Frenchtown, EC measured about 1.5(g/m3, with OC and TC averaging 5.5 (g/m3 and 7 (g/m3  before the fire season.  On 8/13/00 and 8/25/00, EC concentrations averaged 9.41 (g/m3 at Boyd Park and 9.86 (g/m3 at Frenchtown.  OC and TC averages on these dates were 36.61 and 46.00 (g/m3 at Boyd Park, and 35.99 and 45.88 (g/m3 at Frenchtown.  By the end of August, EC, OC, and TC values dropped below their pre-fire season levels.  We suspect that reduced biological activity with the onset of fall is behind these lower levels.

###### SVOCs

The largest spike of SVOCs collected during sampling associated with the fire season came from phenolic compounds.  SVOC data were collected every 12 days at Boyd Park, and every 6 days in Frenchtown.  Levels for the most abundant phenolic species are presented for Boyd Park in Figure 4, and Frenchtown in Figure 5.  Four phenolic compounds showed spikes in their concentrations during the fire season.  These are phenol, 2-methylphenol (o-cresol), 4-methylphenol (p-cresol), and 2,4-dimethylphenol.  Phenolics are not an unexpected by-product of biomass combustion since the lignin content of wood is characterized by phenolic units joined by propane linkers.16               4-Methylphenol showed the highest concentrations during the fire seasons, followed by phenol.  Both 2-methylphenol and 2,4-dimethylphenol showed a strong correlation with one another.  PAHs did not show any strong spikes during the fire season.

VOCs

There were no strong correlations evident between VOC levels and the incidence of active wildland fires.  VOC data were collected every 12 days at Boyd Park, and every 6 days in Frenchtown.  Although there was an increase in toluene in August at Boyd Park, this was probably caused by a reduction in convectional dispersion of automobile emissions in the smoke-impaired valley.  While biomass combustion does lead to emission of benzene, toluene and xylene, their levels will be overwhelmed by that from fossil fuel sources.  The peak evident at Boyd Park in August was far below those seen in winter months when low sun angle and high reflectivity of snow cover also suppress dispersion processes.

#### CONCLUSIONS

The Missoula Valley Sampling Program data collected during the 2000 fire season suggest that the main health impacts to downwind populations reside in the particulate exposures.  The strong correlation of PM2.5 levels and EC-OC-TC levels both support this contention.  These results are consistent with a study conducted in 1994 by Babbitt et al.17  In that study, they concluded that particulate matter was a significant problem at both local and regional levels, but gas concentrations of CO were not high enough to violate national ambient air quality standards.

Since we performed solvent extract on the particulates captured on the PUF samplers, we can also assert that phenolics represent the most abundant organics among the suite of contaminants traveling with the particulates for which we analyzed.  It is worth noting, however, that some PAHs possess higher toxic risks.  Since we have not completed our sampling for the winter season in Missoula, it is premature at this time to assess whether levels seen during the fire season are significantly greater than those seen in residential wood burning particulates during the winter.  Potassium and chloride fingerprints associated with wildland fires offer a handle for source apportionment studies in the future.  A complete listing of all concentrations measured for this study is available from the authors on request.

#### ACKNOWLEDGEMENTS

The authors would like to thank the Missoula City – County Health Department (Jim Carlson, Ben Schmidt, Shannon Therriault), Montana CHEER (Tony Tweedale, Darrel Geist), the Missoula Air Quality Advisory Council, the Missoula City – County Board of Health, and Smurfit – Stone Container Corporation for funding and assistance with the sampling program.

#### REFERENCES

- National Interagency Fire Center Home Page.  http://www.nifc.gov/ (accessed November, 1999).

2.   Montana Fires Home Page.  http://montanafires.com (accessed November, 1999).

3.  Crutzen, P.J.; Andreae, M.O.  Science. 1990, 250, 1669-1678.

- Ryan, P.W.; McMahon, C.K.  Proceedings of the 69th Annual Meeting of the Air Pollution Control Association;  Air Pollution Control Association:  Pittsburgh, PA, 1976.

5.  Hao, W.M.; Scharffe, D.; Lobert, J.M.; et al.  Geophy. Res. Lett. 1991, 999-1002.

6.  Clements, H.B.; McMahon, C.K.  Thermochim. Acta, 1980, 35, 133-139.

7.  Ward, D.E.; Peterson, J.; Hao, W.M. In Proceedings of the Air & Waste Management Association; 1993 Annual Meeting and Exhibition:  Denver, CO, 1993; pp 14-18.

8.  Yokelson, R.J.  “Comments Sent to the Malaysian Meteorological Service in response to a 1997 Request,” The University of Montana – Missoula, 1997:  pp 1-6.

9.  Ward, D.E.;  In Health Hazards of Smoke.  Recommendations of the Consensus Conference April, 1997;  United States Department of Agriculture, Forest Service, Technology & Development Program:  1997; pp 17-28.

10.  Yokelson, R.J.;  Ward, D.E.; Susott, R.A.; Reardon, J.; Griffith, D.W.T. J. Geophys.                               Res., 1997, 102, 18865.

11. Goode, J.G.; Yokelson, R.J.; Susott, R.A.; Babbitt, R.E.; Ward, D.E.; Davies, M.A.; Hao, W.M.  J. Geophys. Res., 2000, 105, 22147.

12. Compendium of Methods for the Determination of Toxic Organic Compounds in Ambient Air.  Second Ed.  Compendium Method TO-13A.  Determination of Polycyclic Aromatic Hydrocarbons (PAHs) in Ambient Air Using Gas Chromatography / Mass Spectrometry (GC/MS).  January, 1999.

13. Method TO-2.  Method for the Determination of Volatile Organic Compounds in 	Ambient Air by Carbon Molecular Sieve Adsorption and Gas Chromatography / 	Mass Spectrometry (GC/MS).  Revision 1.0, April, 1984.

14. Wrobel, C.L. Ph.D. Thesis, The University of Montana, June. 2000.

15. Wilson, W.E.; Suh, H.H.; J. Air & Waste Manage. Assoc. 1997, 47, 1238-1249.

16. Smook, G.A.;  Handbook for Pulp & Paper Technologies.  2nd edition.  Vancouver:  Angus Wilde Publications, Inc., 1992.

17. Babbitt, R.E;, Ward, D.E.; Susott, R.A.; Hao, W.M.; Baker, S.P.;  In Proceedings of 1994 Annual Meeting of Interior West Fire Council:  Coeur d’Alene, Idaho, 1994; pp 1-17.

#### KEY WORDS

# Forest fire

Air pollution

# CMB sampling

Source apportionment

Volatile Organic Compounds

Semi-Volatile Organic Compounds

PM2.5